TRADE OF

Industrial Insulation

PHASE 2

Module 2

Geometry & Pattern Development

UNIT: 10

Flattened Bends & Straights

Produced by

In cooperation with subject matter expert:

Michael Kelly

© SOLAS 2014

Table of Contents

Unit Objective	1

Introduction	2

1.0	Flattened Bends	3

1.1	Applications of Flattened Bends and Straights	3

1.2	Developing a Flattened Bend	4

1.3	Developing a Flattened Bend with Pipes Installed One over the Other	5

2.0	Flattened Straight Sections	6

2.1	Identifying Flattened Straight Sections	6

2.2	Developing a Flattened Straight Section	6

2.3	Swage and Lap Allowances	7

2.4	Fixing Hole Location	7

2.5	Planning and Sequencing	7

Summary	8

# Unit Objective

By the end of this unit each apprentice will be able to:

Explain the concept of flattened forms and state suitable applications.

Draw the half plan and elevation of a flattened form.

Develop a pattern for a flattened form.

# Introduction

Flattened bends and straights are used in industrial insulation applications where pipe-work and tubes are installed too close together to allow for individual lagging and cladding.

# 1.0	Flattened Bends

## 1.1	Applications of Flattened Bends and Straights

Flattened bends and straights are used generally in the following situations:

Frequently, especially with steam boilers, several tubes or pipes are so close together that they cannot be insulated separately but have to be bundled.

External pipe tracing, in which a small bore heating pipe is placed close to the main pipe.

Plant room applications.

Flattened section used to cover main pipe and tracer pipe.

## 1.2	Developing a Flattened Bend

Figure I:	Elevation.

Figure II:	Part Plan view.

Figure III:	Development of a full segment.

Frequently, especially with steam boilers, several tubes or pipes are so close together that they cannot be insulated separately but have to be bundled.

The development of such a bend for a nest of boiler pipes is the same as described earlier for a 90º bend. It must be noted, however, that in figure III the extra section X of figure II has to be interposed between points a and a and points g and g.

Refer to module 2 – unit 7 – Segmented Radius Bends.

## 1.3	Developing a Flattened Bend with Pipes Installed One over the Other

Figure I:	Elevation.

Figure II:	Half a development for a full segment.

First draw figure I similarly as for the normal 90º segmental bend shown earlier in module 2 – unit 7, but with the extra section X added. Draw the quarter circles with centres at points e and f and divide each quarter into three or more divisions. Draw the perpendiculars at points 2 to 9 intersecting the joint line made at points B to J. The lines aA, bB, etc. correspond to the true lengths for the development. Note, however, that the straight line segment X has to be interposed between points e and f.

Refer to module 2 – unit 7 – Segmented Radius Bends.

# 2.0	Flattened Straight Sections

## 2.1	Identifying Flattened Straight Sections

## 2.2	Developing a Flattened Straight Section

Calculate the circumference of the circle using πd.

Calculate the combined straight sections.

Add both measurements together to get the perimeter of the flattened straight section.

Add the allowance for the lap joint.

### Example

Circumference of the circle = πd = 150mm x 3.14 = 471mm

Calculate the combined straights sections = 400mm+ 400mm = 800mm

Perimeter of straight section = 800mm + 471mm = 1271mm

Add allowance for a lap joint = 20mm + 20mm = 40mm

Total material required for straight section = 1271mm+ 40mm

Total: 1311mm

## 2.3	Swage and Lap Allowances

Refer to module 1 – unit 5 – section 3.0 – Lap allowances.

Refer to Module 1 – Unit 7 – section 2.0 – Swaging.

## 2.4	Fixing Hole Location

Refer to module 1 – unit 6 – Marking, Cutting, Punching, Rolling, Seam swaging and Screwing.

## 2.5	Planning and Sequencing

Planning and organisation is vitally important when measuring a large insulation and cladding job. Communication between people and the delegation of tasks will ensure the smooth running of the job. Record keeping, filing of drawings, notes and understanding the works specification are all very important aspects of any job, and a system should be in place whereby information is available in a clear and concise and organised manner.

# Summary

Flattened bends and straights are frequently used in plant rooms and steam boiler rooms where pipe-work and tubes have to be bundled together in order to fit them into the tight spaces. Flattened forms are also used where heat tracer pipes are installed close to the main pipe to allow hat transfer between pipes through direct conduction.

Development of segments of a flattened bend is carried out similarly to that of a radius segmental bend; however the extra straight section must be interposed between points on the development.

Planning and organisation is vitally important when measuring a large insulation and cladding job. Communication between people and the delegation of tasks will ensure the smooth running of the job.

Castleforbes House
Castleforbes Road
Dublin 1

# Text boxes

Module 2

Geometry & Pattern Development

Unit 1

Basic Construction

Unit 6

One Piece Pyramid

Unit 5

Cones and Pyramids

Unit4

Equal and Unequal Tee Pieces

Unit 3

Parallel Line Development

Unit 2

Orthographic Projections

Unit7

Segmented Radius Bends

Unit 8

Triangulation

Unit 9

Tapered or Conical Tee

Unit 10

Flattened Bends and Straights

Unit 11

Valves and Flanges

Unit 12

Eccentric Reducer - Radial Line and Triangulation

### Key Learning Points

Identify applications where flattened forms occur or are required

Layout of plan and elevation

Development of flattened segments. Use of lettering and numbering.

### Key Learning Points

Identification of flattened sections

Determination of true lengths for flattened form

Swag and lap allowances

Fixing hole location

Planning the sequence and efficient drawing layout