| Trade of Metal Fabrication |
| --- |
| Module 1: | Basic Fabrication |
| Unit 11: | Grinding |
|  | Phase 2 |

Table of Contents

List of Figures	4

List of Tables	4

Document Release History	5

Module 1 – Basic Fabrication	6

Unit 11 – Grinding	6

Learning Outcome:	6

Key Learning Points:	6

Training Resources:	6

Exercise:	6

Key Learning Points Code:	6

The Wheel	7

Wheel Inspection	7

Safe Grinding Procedures	8

Personal Protective Equipment	8

The Abrasive Wheel	9

Grade	10

Wheel Selection	10

Material to be Ground	10

Arc of Contact	11

Type of Grinding Machine	12

Process	12

Cutting Off	12

Abrasive Wheel Cutting-Off Machines	13

Portable Grinding Machines	15

Safety	16

Self Assessment	20

Questions on Background Notes – Module 1.Unit 11	20

Answers to Questions 1-3. Module 1.Unit 11	22

Index	24

# List of Figures

Figure 1 - Arc of Contact	11

Figure 2 - Abrasive Wheel Cutting-Off Machine	12

Figure 3 - Portable Electric Grinding Machines	14

Figure 4 - Portable Electric Grinding Machines (continued)	15

Figure 5 – (a) Grinding Welds with Angle Grinder	16

Figure 6 – (b) Angle Grinder used for Bevel Grinding	17

Figure 7 - (c) Grinding Edges of Flame-Cut Apertures with a Straight Grinder	18

Figure 8 - (d) Use of Portable Sander for Metal Surface Finishing	18

Figure 9 - (e) Use of Angle Grinder - Preparing Steel Balustrade Section for Welding on Site	19

# List of Tables

Table 1 - Manufacturer's Type Code	9

# Document Release History

| Date | Version | Comments |
| --- | --- | --- |
| 23/08/06 | First draft |  |
| 13/12/13 | SOLAS transfer |  |

# Module 1 – Basic Fabrication

## Unit 11 – Grinding

Duration – 3 Hours

### Learning Outcome:

By the end of this unit each apprentice will be able to:

Safely set up and operate various grinding machines

Set workrest in accordance with specification

### Key Learning Points:

| Rk | Types of grinding machines – electrical, pneumatic, pedestal, strong/belt. Portable stone/belt. Portable angle/pencil. Composition and use of different types of stone – discs. |
| --- | --- |
| Sk | Use of grinding machines. Changing grind wheels. |
| Sc | Dressing of stones and care and maintenance of wheels in use. |
| Rk H Sk | Eye protection. Loose clothing. Guard. Ratio of speeds between machine and wheels. Precautions to be taken when using the above, i.e. screening, clamping. |
| P | Communication – safe work practice and attitude. |

### Training Resources:

Fabrication workshop facilities.

Grinding machines and wheels. Grind wheel dressing tool. Goggles- visors, P.P.E..

Texts and notes.

### Exercise:

As used in the demonstration of the above.

### Key Learning Points Code:

M = Maths	           D= Drawing     RK = Related Knowledge Sc = Science

P = Personal Skills	Sk = Skill	   H = Hazards

# The Wheel

Due to the nature of its construction the wheel can, if not carefully treated, crack or shatter during use. To reduce the dangers of flying particles causing injury the wheel must be guarded with only the work area exposed. Examine the wheel frequently for cracks or other defects.

When grinding, move the work from side to side to avoid cutting grooves in the wheel. Use the front of the wheel as much as possible. If the side of the wheel is used, avoid using too much force.

# Wheel Inspection

Vitrified bond wheels can be checked with a procedure called the ring test:

Tap the wheel with a non-metal object

If the wheel is in good condition it will ring clearly

Damaged wheels give a dull or chattering sound

# Safe Grinding Procedures

Stand to one side of the grinder when you turn it on, until the wheel reaches operating speed

Slowly and smoothly bring material into contact with the grinding wheel. Avoid bumping

Do not jam work between the wheel and the tool rest

Gradually apply pressure to the wheel. Do not use more pressure than is required for the task

Do not press hard on a dull wheel as this can produce excessive heat which can weaken the wheel, making it more susceptible to shattering

Move the material back and forth over the face of the wheel. This helps prevent grooves from forming

Remember to use the right wheel for the job. If you apply the wrong material to a wheel you may damage it

Do not grind on the side of a wheel unless you are using a machine and wheel designed for side grinding

# Personal Protective Equipment

Eye protection such as safety glasses or goggles must always be worn when using a grinder

Dust masks and hearing protection should also be used

When hot metal is involved face protection and a leather apron may be required

Overalls can be helpful in keeping loose clothing out of the way. Long hair should be tied back and dangling jewellery removed

# The Abrasive Wheel

The abrasive wheel or grinding wheel consists of two constituents:

- The abrasive that does the cutting.

- The bond that holds the abrasive particles together.

The specification of a grinding wheel gives a clue as to its construction and suitability for a particular operation. For example a wheel carrying the marking:

38A60-J5VBE

would indicate that the wheel has an aluminium oxide abrasive; that the abrasive grit is medium to fine in grain size; that the grade is soft; that the structure shows medium spacing; that a vitrified bond is used. How the code marked on the wheel can indicate all this information required in selecting the correct wheel for a particular job will now be examined in some detail.

| Manufacturer’s Type Code | BS Code | Abrasive | Application |
| --- | --- | --- | --- |
| - | A | Aluminium oxide | A high strength abrasive for hard, tough materials |
| 32 | A | Aluminium oxide | Cool; fast cutting, for rapid stock removal |
| 38 | A | Aluminium oxide | Light grinding of very hard steels |
| 19 | A | Aluminium oxide | A milder abrasive than 38A used for cylindrical grinding |
| 37 | C | Silicon carbide | For hard, brittle materials of high density such as cast iron |
| 39 | C | Silicon carbide (green) | For hard, brittle materials such as tungsten carbide |

Table 1 - Manufacturer's Type Code

# Grade

This indicates the strength of the bond and therefore the 'hardness' of the wheel. In a hard wheel the bond is strong and securely anchors the grid in place and therefore reduces the rate of wear. In a soft wheel the bond is weak and the grit is easily detached resulting in a high rate of wear.

The bond must be carefully related to the use of the wheel. If it is too hard the wheel will glaze and become blunt, if it is too soft it will wear away too quickly. This would be uneconomical and also cause loss of accuracy.

| Very Soft | Soft | Medium | Hard | Very Hard |
| --- | --- | --- | --- | --- |
| EFG | HIJK | LMNO | PQRS | TUWZ |

Table 2 – Grade

# Wheel Selection

The correct selection of a grinding wheel depends upon many factors.

## Material to be Ground

(a) An aluminium oxide abrasive should be used on materials with a high tensile strength.

(b) A silicon carbide abrasive should be used on materials with a low tensile strength.

(c) A fine grain wheel can be used on hard brittle materials.

(d) A coarser grain wheel should be used on soft ductile materials. (e) Grade. Use a hard wheel for soft materials and a soft wheel for hard materials.

(f) Structure. A close structured wheel can be used on hard, brittle materials. An open structured wheel should be used on soft, ductile materials.

(g) The bond is seldom influenced by the material being ground.

## Arc of Contact

(a) Figure 1 shows what is meant by 'arc of contact'.

(b) Grain size. For a small arc of contact a fine grain can be used. For a large arc of contact a coarse grain should be used.

(c) Grade. For a small arc of contact a 'hard' wheel can be used. For a large arc of contact a 'soft' wheel should be used.

(d) Structure. For a small arc of contact a close grained wheel can be used. For a large arc of contact an open structured wheel should be used.

Figure 1 - Arc of Contact

## Type of Grinding Machine

A heavy, rigidly constructed machine can produce accurate work using softer grade wheels. This reduces the possibility of 'burning' the workpiece.

## Process

As well as being used for tool sharpening and precision grinding, the abrasive wheel is also used for the following processes:

(a) Dressing the weld and grinding the weld bead flush.

(b) Edge preparation.

(c) Cutting off awkward sections.

Abrasive wheels used for these purposes are subject to far more abuse than those used for precision grinding. They are also required to remove metal more quickly, but they do not have to leave such a good finish or work so accurately as precision grinding wheels.

# Cutting Off

A suitable cutting-off wheel for mild steel would be:

A	24	Q	8	B	or	R

Figure 2 - Abrasive Wheel Cutting-Off Machine

# Abrasive Wheel Cutting-Off Machines

A typical abrasive wheel cutting-off machine is illustrated in Figure 2.

These machines are driven by high power electric motors, the abrasive wheel revolving at speeds in excess of 3000 rev/min.

An adjustable stop is fitted to the counterbalanced head to compensate for wheel wear. A 'vee' belt drives the cutting head from the motor. The diameter of the abrasive wheel is generally about 400 mm and its thickness approximately 3 mm. The section to be cut is clamped in a screw vice, which has a swivelling back-plate for mitre cutting. The head is brought down by hand to sever the material. The high-speed abrasive wheel cuts through steel sections like a knife cutting through butter. Table  shows typical cutting speeds.

| Material Section in. mm. | Cutting Time (in seconds) |
| --- | --- |
| Tube | 1O.D. | 38 O.D. | 2.5 |
| Angle | 3 x 3 x | 76 x 76 x 6.35 | 5 |
| R.S.J. | 3 x 1x | 76 x 38 x 4.76 | 5 |
| Flat bar | 2x | 57.2 x 9.53 | 2 |
| Round bar | 1 Diameter | 25.4 Diameter | 2.5 |
| Channel | 4 x 2 x | 101.6 x 50.8 x 6.35 | 9 |

Table 3 - Typical Cutting Times (Abrasive Cutting-Off Machine)

Figure 3 - Portable Electric Grinding Machines

# Portable Grinding Machines

Portable grinding machines are often used for smoothing down welded joints and seams and generally do much of the fabrication workshop jobs which would otherwise be done by the laborious methods of chiselling and filing.

These portable tools are basically of two types, ELECTRIC and PNEUMATIC, and the three most commonly used variations of portable grinders are:

- THE STRAIGHT GRINDER

- THE ANGLE GRINDER

- THE SANDER GRINDER

Figure 3 and Figure 4 illustrates electrically-powered portable grinders. Figure 3(a) shows a 'straight' portable grinder. This uses an ordinary grinding wheel, cutting on its periphery as in tool grinding.

Usually two sizes are available:

- Grinding wheel diameter 102 mm
Grinding wheel thickness 19 mm
Spindle speed (running light) 8400 rev/min

- Grinding wheel diameter 127 mm
Grinding wheel thickness 19 mm
Spindle speed (running light) 6600 rev/min

Figure 4 - Portable Electric Grinding Machines (continued)

Figure 5 – (a) Grinding Welds with Angle Grinder

## Safety

Hand-powered tools with exposed rotating heads must be switched off and have stopped revolving before being laid down. Otherwise, they can spin themselves off scaffolding, for instance, causing damage and injury.

Power grinders and cutting-off wheels must have guards for protection and to prevent oversize wheels being used.

ALWAYS USE THE CORRECT SIZE AND TYPE OF WHEEL FOR THE JOB - if it is too hard or too fine it becomes glazed. The operator must then use excessive pressure resulting in more breakages and reduced productivity.

Pneumatic grinders must have a mechanical governor to prevent the spindle exceeding its maximum speed.

Figure 6 – (b) Angle Grinder used for Bevel Grinding

Preparation of internal surfaces of large diameter pipe ends for welding.

Figure 7 - (c) Grinding Edges of Flame-Cut Apertures with a Straight Grinder

Figure 8 - (d) Use of Portable Sander for Metal Surface Finishing

Figure 9 - (e) Use of Angle Grinder - Preparing Steel Balustrade Section for Welding on Site

# Self Assessment

# Questions on Background Notes – Module 1.Unit 11

1.    	Draw a Circle 60mm in Diameter.

Clearly show the following:

a.   SECTOR

b.   TANGENT (Shown by a line that is Tangential to Circle)

c.   RADIUS

d.   DIAMETER

2.    	Construct an angle of 45° using a Compass and Rule, clearly show the

intersecting arc’s.

- What are Templates? Give three useful pieces of information on them.

# Answers to Questions 1-3. Module 1.Unit 11

1.

Figure 8. Circle

2.

Figure 9. Angle of 45°

3.

Templates: Templates are used to avoid repetitive measuring and marking-off of the dimensions, where a number of identical parts are required. They can also act as a guide for a cutting process or as a simple means of checking an angle, bend or curve. Templates can be made from Cardboard, Aluminium Timber, Perspex and so on. Typical information found on them would be a job or contact number, size and thickness of the plate drilling requirements, left hand or right hand section.

# Index

A

Abrasive Wheel Cutting-Off Machines, 13

C

Cutting Off, 12

G

Grade, 10

P

Personal Protective Equipment, 8

Portable Grinding Machines, 15

Safety, 16

S

Safe Grinding Procedures, 8

T

The Abrasive Wheel, 9

The Wheel, 7

W

Wheel Inspection, 7

Wheel Selection, 10

Arc of Contact, 11

Material to be Ground, 10

Process, 12

Type of Grinding Machine, 12