| Trade of Metal Fabrication |
| --- |
| Module 1: | Basic Fabrication |
| Unit 1: | Introduction to the Metal Fabrication Trade |
|  | Phase 2 |

Table of Contents

List of Figures	4

List of Tables	4

Document Release History	5

Module 1 – Basic Fabrication	6

Unit 1 – Introduction to the Metal Fabrication Trade	6

Learning Outcome:	6

Key Learning Points:	6

Training Resources:	7

Exercise:	7

Key Learning Points Code:	7

Standard Sections	8

Common Steels used in the Workshop	10

Back Marks and Cross Centres	12

Castella Beams	14

Serial Size – Actual Size	15

Methods of Production	16

Occupational Hazards	20

Noise	20

What is Sound?	20

How Does the Ear Work?	22

Effects of too Much Noise	22

Safe Exposure Level	23

Protective Clothing and Equipment	24

Body Protection	27

Self- Assessment	28

Questions on Background Notes – Module 1.Unit 1	28

Answers to Questions 1-6. Module 1.Unit 1	30

Bibliography	32

Index	33

# List of Figures

Figure 1 - Different Materials/Steels available for Metal Fabrication 1	8

Figure 2 - Different Materials/Steels available for Metal Fabrication 2	9

Figure 3 - Different Materials/Steels available for Metal Fabrication 3	9

Figure 4 - Back Marks	12

Figure 5 - Cross Centres	12

Figure 6 - Pocket Pad Foundation	13

Figure 7 - Roof Truss	13

Figure 8 - Castella Beam	14

Figure 9 - Serial Size	15

Figure 10 - Diagram showing production of the materials in the iron and steel group	16

Figure 11 - The Basic Oxygen Furnace	17

Figure 12 - The Electric Arc Furnace	18

Figure 13 - Blast Furnace	18

Figure 14 - The Ear	22

Figure 15 - Protective Clothing	24

Figure 16 - Protective Eyewear	24

Figure 17 - Protective Equipment	25

Figure 18 - List all instances of unsafe practice that you can detect. (Courtesy of “What’s Wrong” Safety Posters)	26

Figure 19 - Body Protection	27

# List of Tables

Table 1 - Common Steels used in the Workshop	11

Table 2 - Method of Production	19

Table 3 - Examples of the Loudness of Some Noises	21

Table 4 - Noise Levels and Exposure Times  (Equivalent to 90 dB(A) for 8 hours)	23

# Document Release History

| Date | Version | Comments |
| --- | --- | --- |
| 03/08/06 | First draft |  |
| 13/12/13 | SOLAS transfer |  |

# Module 1 – Basic Fabrication

## Unit 1 – Introduction to the Metal Fabrication Trade

Duration – 2 Hours

### Learning Outcome:

By the end of this unit each apprentice will be able to:

Describe the background of the Metal Fabrication industry in Ireland

Describe the most common forms of stock sizes and materials

Describe the contents of the metal fabricator’s tool box

### Key Learning Points:

| P | Craft unions and employer organisations. |
| --- | --- |
| Rk | History, size, scope and trends of the industry -Standard forms of materials -Safe use and handling of tools -Type of work - Platework - Pipework - Structural - Light Fab - Welding - Drawing |
| H | Occupational hazards. |
| Rk | Materials and methods of production. |

### Training Resources:

Lectures, videos, slides, photos, handouts and texts.

### Exercise:

Questions and answers.

### Key Learning Points Code:

M = Maths	           D= Drawing     RK = Related Knowledge Sc = Science

P = Personal Skills	Sk = Skill	   H = Hazards

# Standard Sections

Metals are produced and supplied in many different forms, as shown in Figure 1.

Figure 1 - Different Materials/Steels available for Metal Fabrication 1

Figure 2 - Different Materials/Steels available for Metal Fabrication 2

Figure 3 - Different Materials/Steels available for Metal Fabrication 3

# Common Steels used in the Workshop

150mm x 6mm FB (Flat Bar)

100 x 6 FB

50 x 6 FB

All flat bars listed above are available in different thickness 3mm/5mm etc.

They are known as low carbon steel (LCS).

Standard sheet steel (mild steel plate) is normally available in 8ft. x 4 ft. (2500mm x 1250mm) sections 2mm/3mm, 5mm/6mm, 10mm/12mm etc.

Stainless steel and aluminium are available in the same sizes.

| RSJ = Rolled Steel Joist |  |
| --- | --- |
| BSUB = British Std. Universal Beam |  |
| BSUC = British Std. Universal Column |  |
| RSC = Rolled Steel Channel |  |
| BSEA = British Std. Equal Angle |  |
| BSUA = British Std. Unequal Angle |  |
| RST = Rolled Steel Tees |  |
| Zed Beams (Z Channel) |  |
| Rolled Hollow Section |  |
| Round Hollow Section |  |

Table 1 - Common Steels used in the Workshop

## Back Marks and Cross Centres

A ‘back mark’ is the distance from the heel of an angle or channel section to the centre of a hole in a flange.

Figure 4 - Back Marks

A ‘cross centre’ is the distance between two holes in a flange of a Universal column, beam, rolled steel joist or Tee section.

Figure 5 - Cross Centres

Figure 6 - Pocket Pad Foundation

Figure 7 - Roof Truss

# Castella Beams

This open web beam section is made by cutting the web of a hot rolled joist along a castellated line. The two halves produced are then welded together to form the section illustrated in Figure 8.

The castella beam is one and a half times the depth of the member from which it was cut, and therefore suffers less deflection under load. This section is economical for lightly loaded floors and the openings in the web are convenient for electrical and heating services.

Figure 8 - Castella Beam

# Serial Size – Actual Size

When referring to beams, columns, joists and channels the depth/overall distance from flange to flange is given first followed by the breadth/width of the flange, followed by the mass per metre and finally the length required.

Figure 9 - Serial Size

Although the serial sizes are always referred to on drawings, the actual size of beams, columns etc. can vary considerably. BS41 gives dimensions for serial sizes of sections with mass per metre, actual depth and breadth and thickness of web and flange.

It will be seen that up to seven variations of a serial size is rolled and that the dimensions inside the flanges are constant, while the thickness of the web and flanges vary, hence the variation in serial size and actual size.

# Methods of Production

Figure 10 - Diagram showing production of the materials in the iron and steel group

(The production of tool steel from the Cementation process is now mainly of historical interest only.)

Figure 11 - The Basic Oxygen Furnace

Figure 12 - The Electric Arc Furnace

Figure 13 - Blast Furnace

| Name | Group | Carbon Content % | Some Uses |
| --- | --- | --- | --- |
| Wrought Iron | Wrought Iron | Less than 0.05% | Chain for lifting tackle, crane hooks, architectural ironwork. |
| Dead Mild Steel | Plain Carbon Steels | 0.1 to 0.15 | Sheet for pressing out such shapes as motor-car body, panels, thin wire, rod and drawn tubes. |
| Mild Steel |  | 0.15 to 0.3 | General purpose, workshop bars, boiler plate, girders. |
| Medium Carbon Steel |  | 0.3 to 0.5 0.5 to 0.8 | Crankshafts, forgings, axles, leaf springs, cold chisels. |
| High Carbon Steel |  | 0.8 to 1.0 1.0 to 1.2 1.2 to 1.4 | Coil springs, wood chisels, files, drills, taps and dies, fine edge tools. |
| Grey |  | - | Machine castings. |

Table 2 - Method of Production

# Occupational Hazards

(Note: For further information on Occupational hazards, refer to the Welder on Site…Be Aware video.)

## Noise

A new Statutory Regulation concerning noise at work came into operation on July 1st, 1990.

The full title of this regulation is:

European Communities (Protection of Workers) 
(Exposure to Noise) Regulations, 1990.

Under this regulation FAS (The Training and Employment Authority) is required to provide information to staff, trainees and apprentices on:

what noise is,

the type of damage it can cause,

how it is measured,

what are the safe limits of exposure?

This section attempts to achieve this objective without going into a lot of unnecessary technical data.

### What is Sound?

If we burst a balloon, we cause a disturbance in the surrounding air which may be likened to the effect of throwing a stone in a pond. When the ripples caused by the explosion reach our ears we hear the sound of the balloon burst. It is these ripples travelling through the air that we generally regard as sound.

The human ear is sensitive to noise at frequencies or ripples between 20 times per second and 20,000 times per second. The unit of frequency is the Hertz (Hz). We then speak of the audible range as frequencies or ripples between 20 Hz and 20,000 Hz. We do not use the entire range of frequencies 20-20,000 Hz continuously. A stereo player will emit sound in a range of frequencies from 40-16,000 Hz, whereas a transistor radio covers the range 200-4,000 Hz. In normal speech the frequency range is 125-8,000 Hz but 500-3,000 Hz is the most important area. (20 Hz is a very low bass note, while 20,000 is a very high trebly note).

Loudness is the other factor that is important. We are all aware of it how quiet a whisper is and how loud a jet aircraft engine is. The loudness of a sound is measured in Decibels and this is written as dB(A). The quietest sound the average person can hear is assigned a loudness level of 0 dB(A). The loudest sound we can tolerate without pain is 120 dB(A). Table 3 gives some examples of the loudness of sounds.

| Sound Loudness Level dB(A) | Typical Environment |
| --- | --- |
| 140 | 30m from military aircraft at take-off. | Intolerable |
| 130 | Pneumatic chipping and riveting (operator’s position). | Intolerable |
| 120 | Boiler shop (maximum levels). Ship’s engine room (full speed). | Intolerable |
| 110 | Automatic punch press (operator’s position) sheet metal shop – hand grinding. | Very noisy |
| 100 | Automatic lathe shop. Printing press room. | Very noisy |
| 90 | Heavy lorries at 6m. Construction site – pneumatic drilling. | Very noisy |
| 80 | Kerbside of busy street. Office with tabulating machines. | Noisy |
| 70 | Loud radio (in average domestic room). | Noisy |
| 60 | Restaurant. Department store. | Noisy |
| 50 | Conversational speech at 1m. General office. | Quiet |
| 40 | Average suburban area, whispered conversation at 2m. Residential area at night. | Quiet |
| 30 |  |  |
| 20 | Background in TV and recording studios. | Very Quiet |
| 10 |  |  |
| 0 | Normal threshold of hearing. | Very Quiet |

Table 3 - Examples of the Loudness of Some Noises

### How Does the Ear Work?

The ear is generally considered to have three main sections, the outer, middle and inner ear (see Figure 14). The outer ear consists of the external parts of the ear canal. The middle ear comprises the ear drum and the three bones connecting it to the inner ear. The middle ear can be damaged by traumatic events such as explosion but may be surgically repaired in some cases. The inner ear converts the mechanical (ripples) world of sound to the electrical world of brain. It is the inner part of the ear, called the cochlea, which can be damaged by prolonged exposure to excessive noise.

Figure 14 - The Ear

How noise damages your hearing, when levels are too high. Excessive noise overstimulates the cochlea of the ear which translates sound frequencies into impulses which the brain can interpret. Repeated overstimulation impairs this organ and the damage cannot be repaired.

### Effects of too Much Noise

Most of us have had the experience of being temporarily deafened by exposure to loud noise, whether it is at work, or at a disco. Given a few hours rest, the ear recovers and no permanent damage is done. When exposure is continuous or repeated, however, a gradual hearing loss may result. This hearing loss is permanent and irreversible and is known as "Noise Induced Hearing Loss (NIHL)". It cannot be corrected by surgical or any other means. Even the use of a hearing aid is generally considered unsatisfactory, because of the nature of the hearing loss.

### Safe Exposure Level

Most countries have set a limit of 90 dB(A) for continuous exposure. Ireland adapted this approach in the Noise Regulations 1975 and 1990. It is permissible to have exposures above 90 dB(A), but if so then the duration of such exposure must be limited such that the total anise dose equivalent (Leq) remains below 90 dB(A) aver 8 hours. Table 4 shows such equivalent times.

| Sound Pressure dB(A) | Allowable Exposure Time (per day) |
| --- | --- |
| 90 | 8 hours |
| 93 | 4 hours |
| 96 | 2 hours |
| 99 | 1 hour |
| 102 | 30 minutes |
| 105 | 15 minutes |
| 108 | 7.5 minutes |
| 111 | 3.75 minutes |
| 114 | 112 seconds |
| 117 | 56 seconds |
| 120 | 28 seconds |
| 123 | 14 seconds |
| 126 | 7 seconds |
| 129 | 3.5 seconds |
| 132 | 1.75 seconds |
| 135 | Less than 1 second |

Table 4 - Noise Levels and Exposure Times 
(Equivalent to 90 dB(A) for 8 hours)

## Protective Clothing and Equipment

Figure 15, Figure 16 and Figure 17 illustrate examples of the use of protective clothing and equipment.

Figure 15 - Protective Clothing

Name						Main use

A. Flame-resistant apron			Prevents burning of clothes.

B. Gas welding/cutting goggles		Protects eyes from sparks.

C. Gauntlets					Prevents skin burn.

D. Safety boots (steel toecap)			Prevents crushing of toes.

E. Spats					No molten metal down boots.

F. Boilersuit					Protects neck and chest.

Figure 16 - Protective Eyewear

Name						Use

A. (i) Clear glass				Protects tinted lens.

A (ii) Tinted lens				Limits glare.

B. Goggle body				Stops sparks.

C. Air vent					Prevents misting up.

D. Lens holder					To change broken lens.

E. Strap adjustor				Adjust for size

Figure 17 - Protective Equipment

Name						Use

A. Extractor fan				Takes away fumes.

B. Filter mask					Dust and fumes.

C. Head shield					Prevents skin burn.

D. (i) Renewable clear glass			Takes spatter etc.

D. (ii) Renewable tinted			Prevents arc eye.

E. Leather cape with sleeves			For overhead work.

The filter mask (Figure 17B) is no protection from dangerous gases such as phosgene (which is formed from degreasing agents such as trichloroethylene) or nitrous fumes (caused when large areas of plate are heated) or any other poisonous gases. See safety precautions for TAGS and MAGS.

Note: For more information read Basic Welding and Fabrication.

Figure 18 - List all instances of unsafe practice that you can detect. (Courtesy of “What’s Wrong” Safety Posters)

### Body Protection

Figure 19 - Body Protection

Figure 19 shows a welder fully equipped with protective clothing. The welder's body and clothing must be protected from radiation and burns caused by flying globules of molten metal. It may be necessary for a welder to wear an apron, usually of asbestos or thick leather, to protect his trunk and thighs whilst seated at a bench welding. An apron should also be worn if the welder's clothing is made of flammable material.

When deep gouging or cutting is carried out using metal-arc processes, the amount of 'spatter' is considerably greater than that experienced with normal arc welding, and therefore it is necessary to protect the feet and legs in the same way as the hands and forearms. Suitable leather leggings and spats are available and should be used to prevent burns to the legs, feet, and ankles.

Note: For more information read Fundamentals of Fabrication and Welding Engineering.

# Self- Assessment

# Questions on Background Notes – Module 1.Unit 1

1.     List three occupational hazards associated with the METAL FABRICATION

TRADE?

2.    Name two industries that use pipework and structural steel extensively?

3.    Give one example of what threaded rod is used for?

4.    With the aid of a diagram sketch a section of

- British Standard Equal Angle (B.S.E.A)

- British Standard Unequal Angle (B.S.U.A)

5.    In diagram form, show

- Rolled Steel Channel (R.S.C)

- Universal Beam (U.B)

6.    Taking the method of production into account, give two examples of uses, of both

high carbon steel and dead mild steel.

# Answers to Questions 1-6. Module 1.Unit 1

1.

Noise / Fumes / Arc Flash

2.

a. Pharmaceutical. b. Gas Industry.

3.

Suspended Ceilings: Bolting a steel frame section to a cavity wall, where you would have to thread the nut and washers from outside the block.

4.

Figure 1. (B.S.E.A) Figure 2. (B.S.U.A)

5.

Figure 3. (R.S.C) Figure 4. (U.B)

6.

a. High Carbon Steel: Files / Drills / Coil Springs b. Dead Mild Steel: Motor Vehicle Body’s / Thin Wire / Panels

# Bibliography

Videos:

Understanding welding fumes

Welder on Site…Be Aware (Vocam)

Powered hand tool safety (Vocam)

Industrial Ergonomics (Vocam)

AP video

Abington Publishing

Abington Hall, Abington, Cambridge, CB1 6AH, UK.

Circle organisation Ltd.

Moira Has., Trinity Street,, Dublin 2, Ireland.

Website: www.vocam.com

Books:

Basic Welding and Fabrication	by W Kenyon		ISBN 0-582-00536-L

Fundamentals of Fabrication and Welding Engineering

by FJM Smith		ISBN 0-582-09799-1

printed in Hong Kong AP/01

# Index

B

Bibliography, 30

C

Castella Beams, 14

Common Steels used in the Workshop, 10

Back Marks and Cross Centres, 12

M

Methods of Production, 16

N

Noise

Effects of too Much Noise, 22

How Does the Ear Work?, 22

Safe Exposure Level, 23

What is Sound?, 20

O

Occupational Hazards, 20

Noise, 20

Protective Clothing and Equipment, 24

P

Protective Clothing and Equipment

Body Protection, 27

S

Serial Size – Actual Size, 15

Standard Sections, 8