| Trade of Metal Fabrication |
| --- |
| Module 5: | Pipe Fabrication |
| Unit 7: | Pipe Development Unequal Diameter Oblique 'T' Piece |
|  | Phase 2 |

Table of Contents

List of Figures	4

List of Tables	5

Document Release History	6

Module 5 – Pipe Fabrication	7

Unit 7 – Pipe Development Unequal Diameter Oblique 'T' Piece	7

Learning Outcome:	7

Key Learning Points:	7

Training Resources:	7

Key Learning Points Code:	7

Circles	8

Oblique Intersections & Unequal Pipe Sections	9

Gaskets & Seals: Pipe Intersections	13

Pipes and Fittings	13

Self Assessment	20

Index	21

# List of Figures

Figure 1 - Circles	8

Figure 2 - Right Cylinders	9

Figure 3 - Oblique Cylinders	10

Figure 4 - Two Connecting Pipes	11

Figure 5 - Elbow Joints	12

Figure 6 - Glass Pipe Assemblies	13

Figure 7 - Pipe Fittings and Couplings	14

Figure 8 - Valves	15

Figure 9 - Compression Joints	16

Figure 10 - Graylock Assembly	17

Figure 11 - Standard Joints for Hygienic Piping	18

Figure 12 - Articulated Marine Loading Arm	19

# List of Tables

# Document Release History

| Date | Version | Comments |
| --- | --- | --- |
| 13/02/07 | First draft |  |
| 13/12/13 | SOLAS transfer |  |

# Module 5 – Pipe Fabrication

## Unit 7 – Pipe Development Unequal Diameter Oblique 'T' Piece

Duration – 8 Hours

### Learning Outcome:

By the end of this unit each apprentice will be able to:

Fabricate an off-set oblique “T” piece in unequal pipe sections

Develop intersections in unequal pipe sections

Align flange square to pipe

Describe the use of abrasive discs, pickling, descaling

Calculate density of  material

Calculate approximate length of welded joint

Identify and describe types of gaskets used in pipe gaskets

### Key Learning Points:

| Sk Rk D | Development of oblique intersections in unequal pipe sections. |
| --- | --- |
| Sk Rk D | Indexing of points. |
| Sk Rk | Fabricate pipe intersections. |
| Sk Rk | Alignment of sections and flanges. |
| Rk | Metal protection – surface preparation. |
| M | Mensuration – density. |
| M | Geometry – the circle (proportional area). |
| Rk | Gaskets and seals (rubber, cord, composite materials, cork, o-rings, rope packing). |
| P | Communication, teamwork and safety awareness. |

### Training Resources:

Drawing equipment

Template material

Fabrication workshop and equipment, safety clothing  and equipment

Handouts, notes and technical manuals

Pipe sections M.S. plate

Samples of gaskets and seals

### Key Learning Points Code:

M = Maths	           D= Drawing     RK = Related Knowledge Sc = Science

P = Personal Skills	Sk = Skill	   H = Hazards

# Circles

A circle is a plane figure which is bounded by a curved line called the circumference, which is always the same distance from a fixed point called the centre of the circle. Alternatively we could define a circle by saying that it is the path traced out by a point which moves in a place in such a way that its distance from a fixed point is always constant. This distance from the centre to the circumference is the radius of the circle.

A diameter is a straight line passing through the centre and bounded by the circumference. Clearly the diameter of a circle is twice the radius.

An arc is the name for the part of the circumference between any two points on it.

A chord is a straight line which joins any two points on the circumference.

A segment of a circle is the area which is bounded by a chord and the arc it cuts off.

A sector of a circle is the area which lies between two radii and the arc between them.

A quadrant is the area bounded by two radii which are at right angles to each other and the arc which lies between them. It is a quarter of a circle.

A semi-circle is the area bounded by a diameter and that portion of the circumference which it subtends. As its name implies it is half the area of the circle.

Figure 1 - Circles

# Oblique Intersections & Unequal Pipe Sections

Figure 2 - Right Cylinders

Figure 3 - Oblique Cylinders

Figure 4 - Two Connecting Pipes

Figure 5 - Elbow Joints

# Gaskets & Seals: Pipe Intersections

## Pipes and Fittings

Figure 6 shows exploded views of straight pipe line assemblies showing both the standard and spherical design of end connections.

Pipes and fittings have conical shape or buttress ends with standard flat face or, if required, the ends are spherically ground.

The system ranges from 15 mm to 600 mm bore and fittings are designed to meet all conditions of piping layout within the limits of the allowable pressure/temperature conditions including straight pipes up to 3 metres long.

Figure 6 - Glass Pipe Assemblies

Figure 7 - Pipe Fittings and Couplings

Figure 8 - Valves

Figure 9 - Compression Joints

The coupling was originally applied to copper tube of preferred semi-hard condition, but satisfactory joints can also be made on fully hardened tube. For fully annealed copper tube the coupling should be used only for applications where the pressure is low and where the joints are not required to be broken and re-made frequently.

In the past few years the use of nylon and other types of plastic tubing has increased considerably, mainly as a requirement against corrosion, and the coupling is also applied to semi-rigid plastics and nylon tubing, to soft plastics and to glass tube.

| Type of Coupling | Size Range | Maximum Pressure | Remarks |
| --- | --- | --- | --- |
| Figure 9(a) for metal tube | 1/8 in. (3mm) to 2 in. (50mm) outside diameter in 16 sizes | Hyd. 210 bar to 35 bar Pneum. 70 bar to 11 bar | Pressures according to tube size and based on working temperatures of 30°C |
| Figure 9(b) for nylon tube | 1/8 in. (3mm) to 3/4 in. (19mm) outside diameter in 8 sizes | 42 bar to 14 bar | Up to 60°C and according to size (can be used up to 100°C for intermittent use) |
| Figure 9(c) for soft plastics and glass | 1/8 in. (3mm) to 1/2 in. (12.5mm) bore in 5 sizes | Up to 7 bar (5 bar for 1/2 in size) | Ethylene-vinyl acetate tube, maximum temperature 60°C |

Figure 10 - Graylock Assembly

Figure 11 - Standard Joints for Hygienic Piping

Figure 12 - Articulated Marine Loading Arm

# Self Assessment

Questions on Background Notes – Module 5.Unit 7

No Suggested Questions and Answers.

# Index

C

Circles, 8

G

Gaskets & Seals

Pipe Intersections

Pipes and Fittings, 13

Gaskets & Seals: Pipe Intersections, 13

O

Oblique Intersections & Unequal Pipe Sections, 9

S

Self Assessment, 20