TRADE OF

Pipefitting

PHASE 2

Module 5

Technical Drawing

UNIT: 4

Drawings for Pipe Installation

Produced by

In cooperation with subject matter expert:

Finbar Smith

© SOLAS 2014

Table of Contents

Unit Objective	1

Learning Outcome	2

1.0	System drawings (PFDs and P&IDs)	3

1.1	Process Flow Drawing (PFD)	3

1.2	Process and Instrumentation Drawing (P&ID)	4

2.0	Drawing Practical	6

2.1	Exercise No. 2.5.4a	7

2.2	Exercise No. 2.5.4b	8

2.3	Exercise No. 2.5.4c	10

Exercises	12

Additional Resources	13

# Unit Objective

There are five units in Module 5. Unit 1 focuses on Drawing Methods & Types, Unit 2; Standard Drawing Conventions, Unit 3; Drawing Equipment & Practice, Unit 4; Drawings for Piping Installation, Unit 5; Traceability Record.

In this unit you will be introduced to Drawings for Pipe Installation.

# Learning Outcome

By the end of this unit each apprentice will be able to:

Identify and draw Piping and Instrument Diagram (P&ID) symbols frequently used for valves instruments and equipment as per Exercise No. 2.5.4a

Identify and draw isometric symbols used for piping systems i.e. screwed, butt welded as per Exercise No. 2.5.4b

Identify and draw pipe General Arrangement (GA) symbols that are used for piping general arrangement drawings as per Exercise No. 2.5.4c

Sketch single line piping isometric for 2 of the piping assembly spools

Dimension and label single line piping isometric drawings

Sketch correct piping GA views for 2 of the piping assembly spools

# 1.0	System drawings (PFDs and P&IDs)

## 1.1	Process Flow Drawing (PFD)

A process flow diagram (PFD) is a diagram commonly used in chemical and process engineering to indicate the general flow of plant processes and equipment. The PFD displays the relationship between major equipment of a plant facility and does not show minor details such as piping details and designations.  Typically, process flow diagrams of a single unit process will include the following:

Process piping

Major equipment items

Control valves and other major valves

Connections with other systems

Major bypass and recirculation streams

Operational data (temperature, pressure, mass flow rate, density, etc.).

Process stream names

Process flow diagrams generally do not include:

Pipe classes or piping line numbers

Process control instrumentation (sensors and final elements)

Minor bypass lines

Isolation and shutoff valves

Maintenance vents and drains

Relief and safety valves

Flanges

Process flow diagrams are high levels drawings usually of multiple process systems within a large industrial plant and may be called block flow diagrams or schematic flow diagrams.  Figure 1 illustrates a typical PFD for an evaporator system.

Figure 1 – PFD of Typical Evaporator system

## 1.2	Process and Instrumentation Drawing (P&ID)

The P&ID shows the interconnection of process equipment and the instrumentation used to control the process.  In the process industry, a standard set of symbols is used to prepare P&ID drawings of processes as can be seen in Figure 2 below.  For processing facilities, a P&ID is a pictorial representation of the following:

Key piping and instrument details

Relationship between control instruments and process equipment

Control and shutdown schemes

Safety and regulatory requirements

Basic start up and operational information

Figure 2 – P&ID of Typical compressed air system

As a rule P&IDs do not have a drawing scale and present only the relationship or sequence between components. Just because two pieces of equipment are drawn next to each other does not indicate that in the plant the equipment is even in the same building; it is just the next part or piece of the system. These drawings only present information on how a system functions, not the actual physical relationships.  Because P&IDs provide the most concise format for how a system should function, they are used extensively in the operation, repair, and modification of the plant.

# 2.0	Drawing Practical

Practical Task

This is a practical task. Please refer to relevant sections of the course notes and your instructor for additional information and instruction.

## 2.1	Exercise No. 2.5.4a

## 2.2	Exercise No. 2.5.4b

Figure 3 – Common Isometric Pipe symbols

## 2.3	Exercise No. 2.5.4c

Figure 4- Common GA Pipe symbols

# Exercises

Identify and draw Piping and Instrument Diagram (P&ID) symbols frequently used for valves instruments and equipment as per Exercise No. 2.5.4a

Identify and draw isometric symbols used for piping systems i.e. screwed, butt welded as per Exercise No. 2.5.4b

Identify and draw pipe General Arrangement (GA) symbols that are used for piping general arrangement drawings as per Exercise No. 2.5.4c

Sketch single line piping isometric for 2 of the piping assembly spools from Phase 2, Module 4, Unit 6.

Dimension and label these single line piping isometric drawings

Sketch correct piping GA views for 2 of the piping assembly spools from Phase 2, Module 4, Unit 6.

# Additional Resources

| Title | Author | Ref. Code |
| --- | --- | --- |
| The Induction Book, “Code of Behaviour & Health & Safety Guidelines” | SOLAS |  |
| Basic Welding and Fabrication | W Kenyon | ISBN 0-582-00536-L |
| Fundamentals of Fabrication and Welding Engineering | FJM Smith | ISBN 0-582-09799-1 |
| Workshop processes, practices and materials, 3rd edition, Elsevier Science & Technology | Black, Bruce J 2004 | ISBN-13: 9780750660730 |
| New Engineering Technology | Lawrence Smyth & Liam Hennessy | ISBN 086 1674480 |

Videos:

Understanding welding fumes

Welder on Site…Be Aware (Vocam)

Powered hand tool safety (Vocam)

Industrial Ergonomics (Vocam)

Available from:

Vocam Ireland

Circle Organisation Ltd

Friar Street, Thurles, Co Tipperary, Ireland

Tel: +353 504 24666

Castleforbes House
Castleforbes Road
Dublin 1

# Text boxes

Module 5

Technical Drawing

Unit 1

Drawing Methods & Types

Unit 2

Standard Drawing Conventions

Unit 3

Drawing Equipment & Practice

Unit 4

Drawings for Piping Installation

Unit 5

Traceability Record

### Key Learning Points

Identify the function of a Process Flow Drawing (PFD)

Identify the function of a Process and Instrumentation Drawing (P&ID)

### Key Learning Points

Identify and draw Piping and Instrument Diagram (P&ID) symbols frequently used for valves instruments and equipment

Identify and draw isometric symbols used for screwed and butt welded fittings for piping systems.

Identify and draw pipe General Arrangement (GA) symbols that are used for piping general arrangement drawings

Sketch single line piping isometric for 2 of the piping assembly spools from Phase 2, Module 4, Unit 6.

Dimension and label these single line piping isometric drawings

Sketch correct piping GA views for 2 of the piping assembly spools from Phase 2, Module 4, Unit 6.