| Trade of Sheet Metalwork |
| --- |
| Module 2: | Geometry and Pattern Development |
| Unit 3: | Parallel Line |
|  | Phase 2 |

Table of Contents

List of Figures	5

List of Tables	6

Document Release History	7

Module 2 – Geometry and Pattern Development	8

Unit 3 – Parallel Line	8

Learning Outcome:	8

Key Learning Points:	8

Training Resources:	8

Exercise:	8

Key Learning Points Code:	8

Joint Lines	10

Notching	11

Square Notch	11

45º Notch	11

Straight Notch or Slit	11

Using Patterns	12

Patterns and Drawings	12

Layout or Development	13

Pictorial Drawings	13

Mechanical Drawing	14

Pattern Information Notching	15

Tracing Around a Metal Pattern	15

Transferring a Paper Pattern to Metal	15

Direct Layout on Metal	16

Preparing the Metal	16

Allowances for Seams	16

Making Irregular Curves	17

How to Read the Circumference Rule	17

Self Assessment	19

Index	20

# List of Figures

Figure 1 - Parallel Line Method	8

Figure 2 – Square and Cylindrical Job	11

Figure 3 - Pictorial Drawing	12

Figure 4 - Mechanical Drawing	13

Figure 5 - Fold Lines	13

Figure 6 - Notching	14

Figure 7 - Vice grips	14

Figure 8 - Making Irregular Curves	16

Figure 9 - Reading the Circumference Rule	16

# List of Tables

# Document Release History

| Date | Version | Comments |
| --- | --- | --- |
| 25/07/06 | First draft |  |
| 04/04/14 | 2.0 | SOLAS transfer |

# Module 2 – Geometry and Pattern Development

## Unit 3 – Parallel Line

Duration – 8 Hours

### Learning Outcome:

By the end of this unit each apprentice will be able to:

Discuss the terminology used in the construction of elbows, bends, offsets and tees

Construct and position joint lines, and develop the patterns adding all joint allowances

Develop right cylinders, bends and off-set connection pieces

### Key Learning Points:

| Rk | Determining positions of joint lines. |
| --- | --- |
| D | Development of patterns. |
| Rk | Addition of joint allowances. |
| Rk | Identifying notch removal areas. |
| Rk | Use of division of lines. |
| M | Circumference calculations. |
| D | Developing true shape of cut-outs. |

### Training Resources:

Drawing instruments, materials and equipment

Textbook: The Geometry of Sheet Metalwork

Instructor handouts, drawings

Sheet Metal software packet

### Exercise:

Sample exercise - Figure 1.

### Key Learning Points Code:

M = Maths	           D= Drawing     RK = Related Knowledge Sc = Science

P = Personal Skills	Sk = Skill	   H = Hazards

Figure 1 - Parallel Line Method

# Joint Lines

We always aim to put the joint line on the shortest side. The reason it is put there is to save time and effort.

Sometimes we put the joint elsewhere for appearances of a job or to maximise use of metal.

There are many joints in sheetmetal. Some joints are called self-secured joints. This is where we use the job’s own metal. Examples are Groove joint, Skip joint and Pein joint. They all have different amounts of metal involved in their assembly. It is important to allow for these joints when marking out a pattern.

# Notching

Notching is used to remove portion of the metal to prevent overlapping and bulging on seams and edges.

## Square Notch

The square notch is used on pans and boxes to enable the corners to fit together. The size of the notch is determined by the bend lines on the pattern.

## 45º Notch

The 45° notch made in the form of a V is used when making a knocked up joint or when making a 90° bend on any job with an inside flange. When the bend of an inside flange meets at an angle other than 90°, the notch must be marked to the necessary angle.

## Straight Notch or Slit

An application for the straight notch or slit is shown here.

# Using Patterns

In sheet metal work, a pattern is a piece of material which is cut to the exact size and shape that the sheet metal must be cut in order to be formed into the product desired. Original patterns are usually made on paper. In most cases the pattern will have to be used several times so it is transferred to a piece of metal which becomes a permanent pattern which may be used repeatedly without wear or damage.

# Patterns and Drawings

Sheet metal articles are made of flat pieces of metal cut according to outlines that are drawn or traced on the sheets of metal.

To obtain the correct shape and size, patterns are used. These patterns as explained above may be drawn on paper or directly on the material. It is better for beginners to draw them on paper, since any adjustments when developing can be made saving valuable material. Patterns that are used repeatedly are made of metal and are called master patterns or templates.

The term development refers to the distance across the flat pattern or flat piece of metal before it is formed into shape. See illustration of square and cylindrical job for clarification. The development is the same as the distance round the object.

On a round pipe it would be the circumference.

Figure 2 – Square and Cylindrical Job

# Layout or Development

Layout or development generally refers to the method of developing the lines which form the pattern. The common methods of layout or development are:-

Parallel Line Development

Radial Line Development

Triangulation

# Pictorial Drawings

Pictorial drawings show the object as it actually appears after being formed into shape. Such a drawing is useful to show the shape of the finished object and it is sometimes used in the shop to show simple dimensions. For many objects, the true shape of each side cannot be shown and it becomes difficult to put on clearly understood dimensions. For more complex items a working or mechanical drawing is used.

Figure 3 - Pictorial Drawing

# Mechanical Drawing

A working or mechanical drawing shows the exact size and shape of each side.

Note each view is what you see when looking directly at the various sides.

Since some of the views are alike i.e. top, bottom, front, back, right and left sides, it’s only necessary to draw the number of views required to show the size and shape of the object.

In most cases this will be three; top, front and end views.

Figure 4 - Mechanical Drawing

The term elevation means any view which shows the height of an object. The term plan view means the top view. Front elevation means front view. End elevation means end view. With this type of information, the pattern seen is easily developed.

The X on the lines indicates the place where the metal is to be bent or folded. These lines are called fold lines.

Figure 5 - Fold Lines

# Pattern Information Notching

Notching is used to cut away portions of the metal to prevent overlapping and bulging on seams and edges. Proper notching is very important for a good job and the skill can only be acquired by experience.

Figure 6 - Notching

# Tracing Around a Metal Pattern

When tracing around a metal pattern, it should be held in place by vice grips or some device to prevent the pattern slipping.

Using a scriber or pencil to trace the pattern on the material required.

Figure 7 - Vice grips

# Transferring a Paper Pattern to Metal

Trying to trace around a paper pattern is very difficult since the paper will wrinkle at the slightest pressure. The best method of transferring a pattern from paper to metal is not to cut out the paper pattern at all, but leave it intact on the paper. Then lay it over the metal with weights to keep it from moving, and prick mark through the paper at the ends of all lines and at intervals around curves. Then remove the paper and with a rule and scriber, draw lines connecting all prick marks in the proper manner.

# Direct Layout on Metal

Many experienced workmen do many of their developments directly onto the metal. However for the apprentice it is better to make the more difficult developments on paper and only those for the simple fittings on the metal.

# Preparing the Metal

One of the first steps in preparing to develop a pattern on metal is to square the left end of the metal. Sheet metal is not usually squared accurately before it leaves the factory. The steel square may be used for this purpose, or the sheet may be squared directly by the use of the power or treadle guillotine. The next step is to see that the sheet of metal lies perfectly flat on the bench and not on tools or other equipment.

The measurements for the pattern should be taken from the bottom of the sheet and from the squared-up line at the left end of the sheet. Patterns are always located in the lower left hand corner of the sheet. This practice minimises the waste of metal when cutting out patterns.

# Allowances for Seams

Sheet metal parts are joined by means of seams of various kinds, which we shall deal with in more detail later. The addition of the seams makes it necessary to add material to the pattern.

# Making Irregular Curves

When laying out a pattern on metal, a series of points along an irregular curve are located and then a smooth curve must be drawn through these points. The most common method of doing this is by means of a flexible rule. Made of steel it can be bent and will return to its original shape. A strip of metal the same width as the rule can also be used.

Figure 8 - Making Irregular Curves

# How to Read the Circumference Rule

There are two general methods of finding the circumference of a cy1inder:

- By the use of the circumference rule.

- By the use of formula.

Finding the circumference of a cylinder by the use of the rule is both accurate and simple.

If you examine the rule, you will observe that the upper part of it is used in a manner similar to the ordinary rule. The lower part is used to find the circumference of pipes. The reverse side of the rule is used for finding various angles (degrees).

To read the circumference rule, determine the pipe diameter, i.e. 3" and note the figure in this case 3" on the upper part of the rule as shown in Figure 9.

Figure 9 - Reading the Circumference Rule

Now notice that the divisions on the lower part of the rule represent eights of an inch. Also notice that the figure 3 lines up directly between the third and fourth division reading from 9-10 on the lower part of the rule. The circumference is read as 9 7/16". The circumference rule is usually graduated down to 1/8" and the nearest 1/16" is estimated by the operator or apprentice. Finding the circumference by use of formula.

Occasionally the sheet metal worker needs to find the distance around a pipe without the use of a circumference rule. The method for doing this is to multiply the diameter of the pipe by 3.14 or 3 1/7th. The former is generally preferred. For example, suppose that a pipe 3" in diameter is to be made. The first step would be to find the circumference in inches. This can be done in the following steps:

- Multiply 3.14 by the diameter, 3" 
3.14 
  x 3 
9.42

Change the decimal remainder .42 to a fraction that can be read on the common rule. To do this, multiply the decimal by the denominator of the fraction to be used. The fractions commonly used in sheet metal work are 1/8", 1/16" or 1/32 of an inch, depending upon the degree of accuracy required. For this problem consider that the accuracy should be within the nearest 1/16 of an inch.

Thus:

.42
x 16
 252
   42
6.72 or 7/16"

The decimal .42 is now read as 7/16" so the circumference of a 3 inch pipe would read 9 7/16" on the common rule.
Hence, we see that multiplying the decimal by the denominator of any of the fractional inch graduations on the rule will give the numerator of the desired fraction as shown by the example.

# Self Assessment

# Index

A

Allowances for Seams, 15

D

Direct Layout on Metal, 15

H

How to Read the Circumference Rule, 16

J

Joint Lines, 9

L

Layout or Development, 12

M

Making Irregular Curves, 16

Mechanical Drawing, 13

N

Notching, 10

45º Notch, 10

Square Notch, 10

Straight Notch or Slit, 10

P

Pattern Information Notching, 14

Patterns and Drawings, 11

Pictorial Drawings, 12

Preparing the Metal, 15

T

Tracing Around a Metal Pattern, 14

Transferring a Paper Pattern to Metal, 14

U

Using Patterns, 11