| Trade of Sheet Metalwork |
| --- |
| Module 4: | General Sheet Metalwork |
| Unit 13: | Off-Centre Rectangle to Round |
|  | Phase 2 |

Table of Contents

List of Figures	4

List of Tables	5

Document Release History	6

Module 4 – General Sheet Metalwork	7

Unit 13 – Off-Centre Rectangle to Round	7

Learning Outcome:	7

Key Learning Points:	7

Training Resources:	7

Key Learning Points Code:	7

Self Assessment	9

Answers to Questions 1-4. Module 4.Unit 13	11

Index	13

# List of Figures

Figure 1 - Off-Centre Rectangle to Round	8

# List of Tables

# Document Release History

| Date | Version | Comments |
| --- | --- | --- |
| 21/11/06 | First draft |  |
| 09/04/14 | 2.0 | SOLAS transfer |

# Module 4 – General Sheet Metalwork

## Unit 13 – Off-Centre Rectangle to Round

Duration – 10.5 Hours

### Learning Outcome:

By the end of this unit each apprentice will be able to:

Organise the production sequence

Construct and fabricate an off-centre rectangle to round

Calculate material requirements for pattern development

Assemble and fit a kit form flange to transformer

Identify different developed pattern shapes

### Key Learning Points:

| D | Drawing and development of an off-centre rectangle to round. |
| --- | --- |
| Sk | Shaping and forming of transformers left and right sides. |

### Training Resources:

Toolkit

Propriety flanging

Safety equipment and protective clothing

Tools and machinery/equipment

0.6mm galvanised mild steel

Notepad

Job card

### Key Learning Points Code:

M = Maths	           D= Drawing     RK = Related Knowledge Sc = Science

P = Personal Skills	Sk = Skill	   H = Hazards

Figure 1 - Off-Centre Rectangle to Round

# Self Assessment

Questions on Background Notes – Module 4.Unit 13

1.     What is the “Golden Rule” of triangulation?

2.    What is the area of the round pipe?

3.    What is the circumference of the pipe?

4.    What is the area of the rectangular end?

# Answers to Questions 1-4. Module 4.Unit 13

1.

Plan length against the vertical height of the job: We place the plan length at 90° to the vertical height and measure, the resulting diagonal is the true length.

2.

The formula for area is (R² 3.142 x 75 x 75 = 17673.75mm²

3.

Formula for circumference is 2(R or (D 2 x 3.142 x 75 = 477.3mm or 150 x 3.142 = 477.3mm

4.

Area of rectangle is L x B 250mm x 350mm = 87500mm²

# Index

S

Self Assessment, 9