| Trade of Sheet Metalwork |
| --- |
| Module 4: | General Sheet Metalwork |
| Unit 12: | Square Reducer |
|  | Phase 2 |

Table of Contents

List of Figures	4

List of Tables	5

Document Release History	6

Module 4 – General Sheet Metalwork	7

Unit 12 – Square Reducer	7

Learning Outcome:	7

Key Learning Points:	7

Training Resources:	7

Key Learning Points Code:	7

Square Reducer	9

Self Assessment	11

Answers to Questions 1-2. Module 4.Unit 3	12

Index	13

# List of Figures

Figure 1 - Square to Square Transition	8

# List of Tables

# Document Release History

| Date | Version | Comments |
| --- | --- | --- |
| 21/11/06 | First draft |  |
| 09/04/14 | 2.0 | SOLAS transfer |

# Module 4 – General Sheet Metalwork

## Unit 12 – Square Reducer

Duration – 7 Hours

### Learning Outcome:

By the end of this unit each apprentice will be able to:

Read and interpret drawings involving square reducer

Organise the production sequence

Construct and fabricate a square reducer

Measure, cut, assemble and fit propriety flange

### Key Learning Points:

| D | Drawing and development of a square to square reducer. |
| --- | --- |
| Sk | Shaping and/or forming of transition pieces. |
| Sk | Jointing of transition pieces. |
| Rk | Use and function of transition pieces in ductwork systems. |
| P | Job planning. |

### Training Resources:

Toolkit

Bench stakes

Safety equipment and protective clothing

Notepad

0.6mm galvanised mild steel

Job card

Tools and machinery/equipment

### Key Learning Points Code:

M = Maths	           D= Drawing     RK = Related Knowledge Sc = Science

P = Personal Skills	Sk = Skill	   H = Hazards

Figure 1 - Square to Square Transition

# Square Reducer

- Triangulation is used to develop the pattern. Since the four sides are equal developing one side shall be enough.

- Mark out A Z B (line). Put plan length Z - Z¹ against V.H. of job to obtain true length for pattern.

- The lengths A Z B and 1 Z¹ 2 are all true lengths and taken directly from the plan.

- The distance Z - Z¹ is the same as X - X and so we deduce that the sloping side marked R in the elevation is the true length of all 4 sides needed for developing the pattern. Hence Z¹ - Z in the pattern is the same length as R in the elevation.

- When pattern is developed we put on both ends straight pieces approximately 30mm to facilitate flanges.

- Making the reducer in 4 parts creates 4 joints at the corners. This has to be considered with time spent closing joints, more effective use of material or marking out a full pattern where we have only one joint.

A straight run of duct may be interrupted periodically by a reducer or transition piece. Some pieces like the one in the drawing on the previous page reduce the cross-sectional area. It goes from 300 x 300 to 200 x 200. This is done to maintain the velocity of the air-flow. The further we get away from the air-handling unit the more the air pressure drops. A good system is designed to maintain the original pressure as long as possible.

Technically speaking a reducer reduces the cross-sectional area whereas a transition piece changes the dimensions while still keeping the same area. An example is 400 x 400 changing to 200 x 800 will still give us 160,000 of an area.

The measurements/angles of a transition piece are designed so as to allow air-flow to go through without any obstruction. It is important to stick to the enquiries requirements when fabricating a piece.

# Self Assessment

Questions on Background Notes – Module 4.Unit 12

1.     What are the cross-sectional areas of the two ends of the transition/reducer piece you

just made?

2.    What is the area of one side of the transition?

# Answers to Questions 1-2. Module 4.Unit 3

1.

300 x 300 = 90,000mm² 200 x 200 = 40,000 mm²

2.

Figure 5 The vertical height of the job is 250 but the true length is longer. It is established by the triangulation i.e. 50mm against the 250mm 255 is the true length of the job. A. 300 x 255 = 76,500mm² B. Area of scrap 50 x 255 = 12,750 Subtract B from A 76,500 – 12,750 = 63,750

# Index

S

Self Assessment, 11

Square Reducer, 9