| Trade of Sheet Metalwork |
| --- |
| Module 4: | General Sheet Metalwork |
| Unit 4: | Tee-Piece |
|  | Phase 2 |

Table of Contents

List of Figures	4

List of Tables	5

Document Release History	6

Module 4 – General Sheet Metalwork	7

Unit 4 – Tee-Piece	7

Learning Outcome:	7

Key Learning Points:	7

Training Resources:	7

Key Learning Points Code:	7

Pattern & Elevation of T-Piece	9

Self Assessment	10

Answer to Question 1. Module 4.Unit 4	11

Index	12

# List of Figures

Figure 1 - Tee-Piece	8

Figure 2 - Hole of Penetration - 1/2 Pattern for A	9

# List of Tables

# Document Release History

| Date | Version | Comments |
| --- | --- | --- |
| 13/11/06 | First draft |  |
| 09/01/07 | Implemented edits from Brendan Deasy. |  |
| 09/04/14 | 2.0 | SOLAS transfer |

# Module 4 – General Sheet Metalwork

## Unit 4 – Tee-Piece

Duration – 7 Hours

### Learning Outcome:

By the end of this unit each apprentice will be able to:

Organise production sequence unassisted

Read and interpret drawing for tee-piece

Calculate circumference, material required and production sequence

Produce half-elevation, half-plan and development of hole of penetration

Cut, deburr, roll, groove, swage and braze/assemble tee

### Key Learning Points:

| D | Drawing and development of tee-piece. |
| --- | --- |
| Sk | Fit up of tee-piece/hole of penetration. |
| M | Inside diameters, male and female. |

### Training Resources:

Toolkit

Work sample

Safety equipment and protective clothing

Tools and machinery/equipment

Job card

0.8mm galvanised mild steel

Book – The Geometry of Sheet Metal Work

### Key Learning Points Code:

M = Maths	           D= Drawing     RK = Related Knowledge Sc = Science

P = Personal Skills	Sk = Skill	   H = Hazards

Figure 1 - Tee-Piece

# Pattern & Elevation of T-Piece

Figure 2 - Hole of Penetration - 1/2 Pattern for A

It is important to note that pipe A has to fit on the outside of pipe B. We may reduce the diameter of pipe B to 149 mm and increase A to 151 mm.

When fabricating in the workshop we need only draw pipe A for our elevation with pipe A marked out we sit it on pipe B and trace around it.

# Self Assessment

Questions on Background Notes – Module 4.Unit 4

1.     What is the outside dimension of pipe B and how does it affect pipe A.

Figure 2

# Answer to Question 1. Module 4.Unit 4

1.

It is important to remember the difference between inside and outside dimensions. Pipe B will be 152mm outside and pipe A 150mm inside. This means pipe B is distorted if 150 mm is to fit over 152mm, so we make pipe B 1mm smaller in diameter and pipe A 1mm larger in diameter.

# Index

P

Pattern & Elevation of T-Piece, 9

S

Self Assessment, 10