# MODULE 1 - Induction and Bench Fitting

## Unit 7 – Precision Internal Filing

### Questions

- Files are available in various shapes, list three types.

- List three grades of files.

- What is the purpose of Geometric Tolerancing?

- Explain the term ‘maximum material condition’.

- Explain the terms, Clearance Fit, Minimum Allowance and the Maximum Allowance.

### Answers

1. 	A range of files are available in various shapes such as Flat, Hand, 
 	Warding, Square, Three Square and Half Round.

2. 	Files are cut to the following grades: Rough, Bastard, Second Cut, Smooth 
 	and Dead Smooth.

3. 	Geometric tolerances are used when it is necessary to control more 
 	precisely the form or shape of a feature. It can be used to define 
 	straightness, flatness, roundness, parallelism, perpendicularity, positional, 
 	concentricity etc. It is recommended to use geometric tolerances for parts 
 	that fit together.

4. 	The maximum material condition (MMC) is when the part or a feature 
 	contains the maximum amount of material, e.g. a block of metal with a hole 
 	drilled through, where the external surfaces are at the maximum size 
 	allowed and the hole is at the minimum diameter allowed by the tolerance.

5. 	A clearance fit is when, for example, a shaft at the maximum tolerance is smaller 
 	than a hole that is at the minimum tolerance allowed.

Minimum allowance: This is the difference between the high limit of size of 
 	the shaft and the low limit of size of the hole.

Maximum allowance: This is the difference between the low limit of size of 
 	the shaft and the high limit of size of the hole.