# MODULE 2 – Turning

## Unit 1 – Machine Controls and Operations

### Questions

- Give a brief description of the Headstock on a lathe?

- Give a brief description of the Bed on a lathe?

- What is the purpose of the Carriage and list the main parts.

- How is the size or capacity of the lathe specified?

- What is the purpose of the Saddle?

### Answers

1. 	The Headstock is located on the left hand side of the machine and houses the 
 	gearbox and the spindle.

2. 	The Bed is a strong bridge-like structure made from cast iron. Its upper surface 
 	carries the main slideways.

3. 	The Carriage controls the movement of the cutting tool and consists of the Cross Slide, the Tool Post, the Top Slide, the Saddle and the Apron.

4. 	The capacity of the lathe refers to the size of work that it can accommodate.

5. 	The Saddle is mounted on the guideways of the bed and supports the Cross Slide, the Top Slide Tool Post and the Apron.