# MODULE 3 – Milling

## Unit 6 – Angle Slotting and Reaming

### Questions

- How is an angular surface machined on a workpiece?

- Explain how a workpiece is machine by (i) Tilting the vertical head and       (ii) Tilting the workpiece

- How is the depth of a vee groove measured?

- Calculate the spindle speed for reaming a Ø12mm hole.

- Explain how a slot is machined at an angle in a mild steel block.

### Answers

- Angular surfaces can be machined by either (i) tilting the vertical head (ii) tilting the workpiece or (iii) using a chamfering tool.

- Tilting the vertical head: This is achieved by rotating the head by the required angle using the graduations on the head of the machine. The workpiece is held in the vice and machined at the inclined angle.

Tilting the workpiece: This is done by setting up the workpiece in a standard 
 	machine vice at the required angle, which can be aligned with a protractor or 
 	with a sine bar and slip gauges. The workpiece can also be setup in a universal 
 	vice, which can be tilted to the required angle using graduations on the vice and 
 	then locked in place

3. 	The depth of the vee groove is measured by placing a roller gauge in the vee 
 	and setting up two equal piles of slip gauges or parallels on the top flat surface. 
 	A depth micrometer is then used to measure the distance from the slip gauges to 
 	the top of the roller gauge. The roller diameter and the height in relation to the 
 	datum is normally specified on the drawing.

4. 	To find the correct RPM (revs per minute) for a Reamer, use the RPM formula to get the spindle speed for the corresponding size Drill and divide the answer by two to get the Reamer spindle speed.

RPM = Cutting Speeds in metres per minute x 1000 Circumference of cutter in millimetres = S x 1000 л x D

Using a typical cutting speed of 30 meters/min for mild steel and 3.14 for л, the spindle speed is calculated as follows:

RPM (Drill) = 30 x 1000 3.14 x 12 = 796

RPM (Reamer) = 796 2 = 398

5. 	When machining a slot at an angle, the vice can be rotated by the required angle 
 	using the graduations at the side of the vice. To get a more accurate angle, angle 
 	gauge blocks or a sine bar can setup as explained above and a dial indicator can 
 	be run along its length and the vice adjusted until the clock runs true.