TRADE OF

Pipefitting

PHASE 2

Module 4

Pipe Installation

UNIT: 6

Piping System Assembly

Produced by

In cooperation with subject matter expert:

Finbar Smith

© SOLAS 2014

Table of Contents

Unit Objective	1

Learning Outcome	2

1.0	Piping System Assembly	3

1.1	Exercise No. 2.4.6a	4

1.2	Exercise No. 2.4.6b	5

1.3	Exercise No. 2.4.6c	6

1.4	Exercise No. 2.4.6d	7

1.5	Exercise No. 2.4.6e	8

1.6	Exercise No. 2.4.6f	9

1.7	Exercise No. 2.4.6g	10

Exercises	11

Additional Resources	12

# Unit Objective

There are six Units in Module 4. Unit 1 focuses on Introduction to Pipe Installation and Safety, Unit 2; Piping Services, Unit 3; Electricity on Site, Unit 4; Bracket Fabrication, Unit 5; Ancillary Piping Equipment and Unit 6; Piping system assembly.

This unit identifies how best to approach a practical task and how proper planning and preparation can help contribute to ensuring a project is completed on time.

# Learning Outcome

By the end of this unit each apprentice will be able to:

Read and interpret engineering drawings as per Excerise No.s 2.4.6a, 2.4.6b, 2.4.6c, 2.4.6d and 2.4.6e in orthographic projection.

Quantify materials for given project and complete BOM as per Excerise No.s 2.4.6a, 2.4.6b, 2.4.6c, 2.4.6d, 2.4.6e, 2.4.6f and 2.4.6g

Plan work sequence section of the project.

Gather pipe, fittings and components required to make Spools 1 and 2 as per BOM.

Mark out, cut, thread, fit and assemble components for Spool 1 and 2 as per Excerise No.s 2.4.6a and b.

Gather pipe, fittings and components required to make Spool 3 as per BOM.

Mark out, cut, glue, fit and assemble components for Spool 3 as per Excerise No. 2.4.6c

Gather pipe, fittings and components required to make Spool 4 as per BOM.

Mark out, cut, fit, assemble components and tighten compression joints for Spool 4 as per Excerise No. 2.4.6d.

Gather pipe, fittings and components required to make 20L vessel as per BOM.

Mark out, cut, fit and weld components for 20L vessel as per Exercise No. 2.4.6e

Gather pipe, fittings and components required to make heat exchanger as per BOM.

Mark out, cut, fit and weld components for heat exchange as per Excerise No. 2.4.6f

Assemble and bracket piping system assembly as per Excerise No. 2.4.6g

Prepare and pressure test pipe assembly.

Dismantle piping system assembly and restock reusable parts.

# 1.0	Piping System Assembly

Practical Task

This is a practical task. Please refer to relevant sections of the course notes and your instructor for additional information and instruction.

## 1.1	Exercise No. 2.4.6a

## 1.2	Exercise No. 2.4.6b

## 1.3	Exercise No. 2.4.6c

## 1.4	Exercise No. 2.4.6d

## 1.5	Exercise No. 2.4.6e

## 1.6	Exercise No. 2.4.6f

## 1.7	Exercise No. 2.4.6g

# Exercises

Complete practical project as directed in exercise sheets 2.4.6a to 2.4.6g

# Additional Resources

| Title | Author | Ref. Code |
| --- | --- | --- |
| The Induction Book, “Code of Behaviour & Health & Safety Guidelines” | SOLAS |  |
| Basic Welding and Fabrication | W Kenyon | ISBN 0-582-00536-L |
| Fundamentals of Fabrication and Welding Engineering | FJM Smith | ISBN 0-582-09799-1 |
| Workshop processes, practices and materials, 3rd edition, Elsevier Science & Technology | Black, Bruce J 2004 | ISBN-13: 9780750660730 |
| New Engineering Technology | Lawrence Smyth & Liam Hennessy | ISBN 086 1674480 |

Videos:

Understanding welding fumes

Welder on Site…Be Aware (Vocam)

Powered hand tool safety (Vocam)

Industrial Ergonomics (Vocam)

Available from:

Vocam Ireland

Circle Organisation Ltd

Friar Street, Thurles, Co Tipperary, Ireland

Tel: +353 504 24666

Castleforbes House
Castleforbes Road
Dublin 1

# Text boxes

Module 4

Pipe Installation

Unit 1

Introduction to Pipe installation and Safety

Unit 2

Piping Services

Unit 3

Electricity on Site

Unit 4

Bracket Fabrication

Unit 5

Ancillary Piping Equipment

Unit 6

Piping System Assembly

### Key Learning Points

Read and interpret engineering drawings for the project.

Quantify materials for the given project and complete an accurate Bill of Materials for the project

Plan a correct sequence of work for the project

Assemble all the required tools and materials required to complete the project

Mark out, cut, fit and weld all the components required to complete the project

Test all pipework and assemble all components to complete the project.