| Trade of Sheet Metalwork |
| --- |
| Module 2: | Geometry and Pattern Development |
| Unit 1: | Basic Construction |
|  | Phase 2 |

Table of Contents

List of Figures	4

List of Tables	4

Document Release History	5

Module 2 – Geometry and Pattern Development	6

Unit 1 – Basic Construction	6

Learning Outcome:	6

Key Learning Points:	6

Training Resources:	7

Exercise	7

Key Learning Points Code:	7

Geometry	10

To Locate the Centre of an Arc or a Circle 'A'	10

B - How to Construct a Right-Angle in a Semi-Circle	10

C - How to Construct an Ogee Curve	11

Tangential Arcs	12

Self Assessment	13

Index	14

# List of Figures

Figure 1 - Basic Construction 1	8

Figure 2 - Basic Construction 2	9

Figure 3 - A - To locate the Centre of a given Arc or Circle	10

Figure 4 - B - To Construct a Right-Angle Triangle in a Semi-Circle	10

Figure 5 - C - To Construct an Ogee Curve	11

Figure 6 - Tangential Arcs	12

# List of Tables

# Document Release History

| Date | Version | Comments |
| --- | --- | --- |
| 19/07/06 | First draft |  |
| 04/03/14 | 2.0 | SOLAS transfer |

# Module 2 – Geometry and Pattern Development

## Unit 1 – Basic Construction

Duration – 7 Hours

### Learning Outcome:

By the end of this unit each apprentice will be able to:

Identify and use standard drawing equipment

- Identify and draw types of lines used in technical drawing

- Construct, bisect and divide lines and angles

- Construct circles and tangents

- Locate tangent points and arc centres

- Comprehend the fundamentals of geometric construction

- Use scale rule

### Key Learning Points:

| Rk D | Use and meaning of lines |
| --- | --- |
| D | Use of drawing instruments |
| D | Construction, bisection and division of straight lines |
| D | Construction, bisection and division of angles |
| D | Location of arc centres |
| Rk | Location of tangent points |
| Rk | Use of scale rule |

### Training Resources:

Drawing instruments, equipment and materials

Textbook: The Geometry of Sheet Metalwork

Instructor handouts, drawings

### Exercise

Sample exercise – Figure 1 and Figure 2.

### Key Learning Points Code:

M = Maths	           D= Drawing     RK = Related Knowledge Sc = Science

P = Personal Skills	Sk = Skill	   H = Hazards

Figure 1 - Basic Construction 1

Figure 2 - Basic Construction 2

# Geometry

## To Locate the Centre of an Arc or a Circle 'A'

Select three points C, D and E on the arc AB. Bisect the arc lengths between these points, using C, D and E as centres. The point O where the bisectors intersect will be the centre of the given arc or circle.

Figure 3 - A - To locate the Centre of a given Arc or Circle

## B - How to Construct a Right-Angle in a Semi-Circle

Select any point C on the circumference of the given semicircle and draw lines from the diameter to termination points A and B to C. Then the angle ACB is 90°. Similarly the angles at E and D are right-angles.

Figure 4 - B - To Construct a Right-Angle Triangle in a Semi-Circle

## C - How to Construct an Ogee Curve

The termination points of the curve AB are normally given dimensionally. Join A and B by a straight line and bisect it at C. With radius R equal to the required radius of the curve, and with points A, C and B as centres, draw arcs to locate D and E. With the radius and centres D and E complete the curve.

Figure 5 - C - To Construct an Ogee Curve

## Tangential Arcs

Figure 6 shows the constructions associated with tangential arcs. Fig. A shows the construction for an arc that is tangential to a circle and a straight line. Construct a parallel line, at a distance equal to the given radius R1, to the given straight line AB. Add R1 to the radius R of the given circle and from the centre of the circle draw an arc to locate point O. With centre O and radius R1 draw the required arc to touch the straight line and the circle.

Fig. B shows the construction of the external, tangential arc. Let R represent the radius of the given arc, and R1 and R2 the radii of the circles it is required to touch. Subtract the circle radii from the given radius of the arc, in turn, and from the respective centres of the circles draw arcs to intersect at point O. With O as centre and radius R draw the required arc to touch the circles externally.

Fig. C shows the construction of the internal, tangential arc. Add the circle radii to the given radius of the arc R. From the respective centres of the circles draw arcs to intersect at a point O. With O as centre and radius R, draw the required arc to touch the circles internally.

Figure 6 - Tangential Arcs

# Self Assessment

# Index

G

Geometry, 10

B - How to Construct a Right-Angle in a Semi-Circle, 10

C - How to Construct an Ogee Curve, 11

Tangential Arcs, 12

To Locate the Centre of an Arc or a Circle 'A', 10