| Trade of Sheet Metalwork |
| --- |
| Module 2: | Geometry and Pattern Development |
| Unit 5: | Oblique Cylinders |
|  | Phase 2 |

Table of Contents

List of Figures	4

List of Tables	5

Document Release History	6

Module 2 – Geometry and Pattern Development	7

Unit 5 – Oblique Cylinders	7

Learning Outcome:	7

Key Learning Points:	7

Training Resources:	7

Exercise:	7

Key Learning Points Code:	7

Oblique Cylinders	8

Exercise	8

Developed Pattern Procedure	9

Self Assessment	10

Index	11

# List of Figures

Figure 1 - Oblique Cylinders	8

Figure 2 - Developed Pattern	9

# List of Tables

# Document Release History

| Date | Version | Comments |
| --- | --- | --- |
| 26/07/06 | First draft |  |
| 31/03/14 | 2.0 | SOLAS transfer |

# Module 2 – Geometry and Pattern Development

## Unit 5 – Oblique Cylinders

Duration – 8 Hours

### Learning Outcome:

By the end of this unit each apprentice will be able to:

Identify the properties of the oblique cylinder

Identify the geometrical differences between the right cylinder and the oblique cylinder

Develop patterns for oblique cylinders cut by angular and curved planes

Develop true shape of holes of intersection

### Key Learning Points:

| D | Plan and elevation layout. |
| --- | --- |
| D | False length radials. |
| D | True length radials. |
| D | Transferral of points from false lengths to true lengths. |
| D | Oblique cylinder cutting planes. |
| D | Intersection of oblique cylinders. |
| Rk | Joint location/positioning. |
| D | Oblique pattern development. |

### Training Resources:

Drawing instruments, equipment and materials

Textbook: The Geometry of Sheet Metalwork

Instructor handouts, drawings

### Exercise:

Sample exercise - Figure 1.

### Key Learning Points Code:

M = Maths	           D= Drawing     RK = Related Knowledge Sc = Science

P = Personal Skills	Sk = Skill	   H = Hazards

Figure 1 - Oblique Cylinders

# Oblique Cylinders

## Exercise

Answer Sample Questions

Fig. 1 shows the elevation of an oblique cylinder. Develop the full template to the dimensions given.

Fig. 2 shows the junction of two oblique cylinders. Draw the elevation given and develop the full template for one leg, placing the seam on the short side. Scale: 1:10.

The elevation of intersecting cylinders of equal diameter is shown in Fig. 3. Develop the full template for each cylinder with the seam on the short side. Scale: 1:5.

The inlet to a square tank is shown in elevation in Fig. 4. Develop the full template for the cylindrical member with the seam at SS and draw also the true shape of the hole required in the tank. Scale: 1:2.

The elevation of an elliptical tank is shown in Fig. 5; the bottom is a circular plate 350 mm in diameter. Develop the full template, locating the seam on the short side. Scale: 1:5.

Figure 2 - Developed Pattern

## Developed Pattern Procedure

- Draw plan and elevation.

- Divide the base on the plan into a number of parts, e.g. 12.

- Bring these divisions up to the base in elevation, and then up parallel to the learning edge, as shown.

- Project each division line on the elevation at right angles.

- Choose a starting point A and with radius L from the plan, swing an arc B. Find B.

- Continue to locate other points.

- Construct the panels and add top and base.

# Self Assessment

# Index

O

Oblique Cylinders, 8

Developed Pattern Procedure, 9

Exercise, 8