| Trade of Sheet Metalwork |
| --- |
| Module 2: | Geometry and Pattern Development |
| Unit 2: | Orthographic Projections |
|  | Phase 2 |

Table of Contents

List of Figures	4

List of Tables	4

Document Release History	5

Module 2 – Geometry and Pattern Development	6

Unit 2 – Orthographic Projections	6

Learning Outcome:	6

Key Learning Points:	6

Training Resources:	7

Exercise:	7

Key Learning Points Code:	7

Drawing	11

Third Angle Projection	12

Selection of Views	13

Self Assessment	15

Index	16

# List of Figures

Figure 1 - Orthographic Projection 1	8

Figure 2 - Orthographic Projection 2	9

Figure 3 - Visualise the Metal Part Suspended in a Hinged Glass Box	10

Figure 4 - Orthographic Drawing	11

Figure 5 - (a) First-Angle and (b) Third-Angle Projection	11

Figure 6 - Orthographic Drawing: Geometric Construction	12

Figure 7 - Third-Angle Orthographic Drawing	12

Figure 9 – Two-View Shapes Drawn in Third-Angle	13

# List of Tables

# Document Release History

| Date | Version | Comments |
| --- | --- | --- |
| 24/07/06 | First draft |  |
| 04/04/14 | 2.0 | SOLAS transfer |

# Module 2 – Geometry and Pattern Development

## Unit 2 – Orthographic Projections

Duration – 10 Hours

### Learning Outcome:

By the end of this unit each apprentice will be able to:

State the differences between first and third angle orthographic projections

Construct simple orthographic drawings in 1st and 3rd angle

Visualise sheet metal components from drawings

Interpret information from blueprints and working drawings

Use dimensioning techniques and conventional symbols

Make sketch of sheet metal components

### Key Learning Points:

| D | Planes of projection. |
| --- | --- |
| D | Relative positions for 1st and 3rd angle orthographic projection. |
| Rk | Information transfer from one view to another. |
| Rk | Drawing construction techniques. |
| Rk | Component visualisation from drawings. |
| Rk | Read and understand working drawings. |
| D | Dimensioning techniques and symbols. |
| D | Plans, elevations and end views. |
| D | Profile views. |
| D | Freehand sketching. |

### Training Resources:

Drawing instruments, equipment and materials

Instructor handouts, drawings

Textbook: The Geometry of Sheet Metalwork

### Exercise:

Sample exercise drawings: Figure 1 to Figure 8.

### Key Learning Points Code:

M = Maths	           D= Drawing     RK = Related Knowledge Sc = Science

P = Personal Skills	Sk = Skill	   H = Hazards

Figure 1 - Orthographic Projection 1

Figure 2 - Orthographic Projection 2

Figure 3 - Visualise the Metal Part Suspended in a Hinged Glass Box

To grasp the theory of orthographic projection, visualise the metal part suspended in a hinged glass box.

# Drawing

In order to interpret orthographic drawings correctly it is very important for the craftsman to be able to distinguish between first- and third-angle projections. Any misinterpretation, even of a relatively simple component, will result in some details being fabricated in the Opposite hand. In Figure 5 the same component is shown drawn (a) in first-angle (English) projection, and (b) in third-angle (American) projection, for comparison of the two methods.

Figure 4 - Orthographic Drawing

Figure 5 - (a) First-Angle and (b) Third-Angle Projection

## Third Angle Projection

It will be noticed in Figure 5 that a drawing in third-angle projection has exactly the same views as the first-angle projection, but the views are positioned in a different relationship to each other. Figure 4 shows how the views are conventionally positioned in a third-angle drawing. Figure 6 illustrates the geometrical construction employed to produce the views given in Figure 4. To avoid confusion the projection used must always be clearly stated on the drawing.

Figure 6 - Orthographic Drawing: Geometric Construction

Figure 7 - Third-Angle Orthographic Drawing

The figure shown here illustrates the geometrical construction used to produce the views given in Figure 7.

The component is first built up using fine and feint construction lines; component is then 'lined in' more heavily so that it stands out.

Note: Except for a complex development or a constructed curve, full geometric construction is seldom used in the drawing office.

## Selection of Views

In practical work it is important to choose the combination of views that will describe the shape of a component in the best and most economical way. Often only two views are necessary.

For example, a cylinder, if on a vertical axis, would require only a front elevation and a plan view. If the cylinder is on a horizontal axis, only a front elevation and an end view is required. Conical and pyramidal shapes can also be described by two views. Figure 8 illustrates two-view shapes drawn in third-angle projection.

Sometimes two views are used to describe an object or component on the assumption that the contour in the third direction is of a shape that can naturally be expected. Figure 8 explains why in many cases two views do not fully describe the shape of a component.

The two views shown at (a) would suggest that component 'A' is rectangular and of square cross-section.

Figure 8 – Two-View Shapes Drawn in Third-Angle

However, these two views may be the front elevation and plan views of the tapering rectangular component 'A' as shown in the two views at (b). The two views of a component shown at (c) do not describe the component at all. It might be assumed to be of square cross-section, but it could as easily be of round, rectangular, quarter-round, or of any other shaped cross-section, which can only be indicated by a side view. The figure at (d) illustrates how the component shown at '8' is clearly described by two views. In practice, any simple component would be visualised mentally and the necessary views selected without a pictorial sketch. However, in more complicated work, a pictorial sketch may be used to advantage. It is never necessary to sketch all possible views in order to make a selection.

# Self Assessment

# Index

D

Drawing, 12

Selection of Views, 14

Third-Angle Projection, 13