| Trade of Sheet Metalwork |
| --- |
| Module 4: | General Sheet Metalwork |
| Unit 14: | Conical Reducer |
|  | Phase 2 |

Table of Contents

List of Figures	4

List of Tables	5

Document Release History	6

Module 4 – General Sheet Metalwork	7

Unit 14 – Conical Reducer	7

Learning Outcome:	7

Key Learning Points:	7

Training Resources:	7

Key Learning Points Code:	7

Right Cone (Radial Line)	9

Triangulation	9

Density	10

To Find the Density of an Irregular Solid	11

Relative Density (Specific Gravity)	12

Density	12

Physical Properties of Materials	13

Mass, Volume, Density	14

Self Assessment	16

Answers to Questions 1-5. Module 4.Unit 14	18

Index	20

# List of Figures

Figure 1 - Conical Transition Piece	8

Figure 2 - Development of a Right Cone Frustrum (Radial Line)	9

Figure 3 - Development of a Truncated Cone (Triangulation)	9

Figure 4 – Density	10

Figure 5 - Finding the Density of an Irregular Solid	11

# List of Tables

Table 1 - Some Common Densities g cm	11

# Document Release History

| Date | Version | Comments |
| --- | --- | --- |
| 22/11/06 | First draft |  |
| 08/04/14 | 2.0 | SOLAS transfer |

# Module 4 – General Sheet Metalwork

## Unit 14 – Conical Reducer

Duration – 7 Hours

### Learning Outcome:

By the end of this unit each apprentice will be able to:

Read and interpret drawings involving conical triangulation

Calculate material requirements for pattern development

Organise the production sequence

Produce and fabricate a conical reducer using the triangulation method

### Key Learning Points:

| D | Drawing and development of a conical transition piece/reducer. |
| --- | --- |
| Rk | Where to use triangulation with conical transitions (i.e. unobtainable apex). |
| Rk | Methods used to arrive at conditions of development. |
| H | Safety in assembly. |
| M | Density/specific gravity. |

### Training Resources:

Toolkit

0.6mm galvanised mild steel

Conical bench stakes

Tools and machinery/equipment

Safety equipment and protective clothing

Spot welder, pedestal/handtype, pedestal

Notepad

Job card

### Key Learning Points Code:

M = Maths	           D= Drawing     RK = Related Knowledge Sc = Science

P = Personal Skills	Sk = Skill	   H = Hazards

Figure 1 - Conical Transition Piece

# Right Cone (Radial Line)

Figure 2 - Development of a Right Cone Frustrum (Radial Line)

# Triangulation

Figure 3 - Development of a Truncated Cone (Triangulation)

# Density

Would you say that coal is heavier than wool? Careful! You could be wrong. Look at the two men in the figure shown here. When comparing substances in this way we should compare the same volume of each substance, e.g. 1 cubic centimetre of each.

Figure 4 – Density

Density = mass/volume

If a piece of iron of mass 39 g has a volume of 5 cm³, what is its density?

The mass of 5 cm³ = 39 g

→ 	the mass of 1 cm³ = 39g/5cm³ = 7.8 g cm³.

Mathematically we can now say that

where p is the density and v is the volume.

## To Find the Density of an Irregular Solid

- Use a balance to find the mass of the solid.

- Fill the overflow can with water and allow the excess to drip away.

- Place a graduated cylinder under the spout.

- Lower the solid gently into the overflow can.
The volume of water which overflows into the cylinder equals the volume of the solid.

- Now divide the mass by the volume.

Figure 5 - Finding the Density of an Irregular Solid

| Aluminium | 2.7 | Silver | 10.5 |
| --- | --- | --- | --- |
| Copper | 8.9 | Zinc | 7.1 |
| Gold | 19.3 | Mercury | 13.6 |
| Iron | 7.8 | Meths | 0.8 |
| Lead | 11.4 |  |  |

Table 1 - Some Common Densities g cm

The S.I. unit of density is kg m  , but g cm   is more convenient.

E.g. since the density of water is taken as 1 g cm   and the density of mercury is 13.6 g cm  , then the relative density of mercury is 13.6.

## Relative Density (Specific Gravity)

The weight of a substance per volume, compared to an equal volume of water. For example, 1 m³ of water weighs 1000 kg at 4°C whereas 1 m³ of lead weighs about 11 300 kg; thus it can be seen that lead is 11.3 times heavier. From this we can calculate the weight of any substance by dividing the density of a substance by the density of water. Water is always shown with a specific gravity number of 1.0; therefore any material with a number higher than 1. a will sink in water and those with a number less than 1.0 will float.

The relative density of gases can also be measured and are compared with the specific gravity of air which is also expressed as 1.0.

It is worth noting that we can compare materials with each other; for example, we can see that cast iron weighs less than tin per equal volume and that natural gas is lighter than air and will rise upwards should there be a leak.

## Density

Density is the number of molecules per volume in a particular substance. As previously stated, 1 m³ of water at 4°C weighs 1000 kg whereas a cubic metre of water at 82°C weighs only 967 kg; thus it can be seen that the water at the lower temperature is heavier, there being more molecules, and that the molecules are closer or 'more dense' (more compact).

Water, when cooled below 4° Celsius, begins to expand again; this is a strange phenomenon peculiar to water. It will be seen that water is at its maximum density at 4°C.

# Physical Properties of Materials

The term physical properties refers to the weight, colour and strength etc. of a material. All materials have their own qualities and properties, the meaning of each being identified as follows:

Density	The mass of molecules per volume in a particular substance, thus the weight, e.g. kg/m³ (see relative density).

Relative density	(also called specific gravity) The weight of a substance compared to an equal volume of water. Water has a relative density of 1; materials with a number greater than 1 sink of water.

Specific heat		The amount of heat required to raise 1 kg of material by 1°C.

# Mass, Volume, Density

The density of water is 1,000 kg per cubic metre; this means that a water tank of volume 1m³ when full with water has a mass of 1,000 kg (neglecting mass of tank).

Example:

Calculate the volume and mass of water which a storage tank of length 0.8m, width 0.4 m, and height 0.5m would contain when completely full. Density of water is 1,000 kg/m³.

Volume = 0.8 x 0.4 x 0.5 = 0.16 m³.

Mass of water = 0.16 x 1,000 = 160 kg.

Another useful relationship is that a mass of 1 kg of water occupies a volume of 1 litre. There are 1,000 litres in 1 cubic metre.

Test Yourself:

Calculate the volume of water in a pipe of diameter 100 mm and length 1m. Express the volume in cubic metres and litres. State the number of mm³ in 1 litre.

Volume 		= π r² 1

= 3.14 x 50 x 50 x 1, 000

Answer:

= 0.00785m²

Volume in litres 	= 0.00785 x 1, 000

= 7.85 litres

1 litre 		= 1,000,000 mm³

A list of densities of common gases, liquids and materials is given below:

Air 	1.3 kg/m³

Petrol 	750 kg/m³

Water 	1,000 kg/m³

Aluminium 	2,600 kg/m³

Mild Steel 	7,300 kg/m³

Cast Iron 	7,800 kg/m³

Brass 	8,200 kg/m³

Copper 	8,700 kg/m³

Lead 	11,400 kg/m³

Mercury 	13,600 kg/m³

Example:

Calculate the volume and mass of a piece of mild steel 100 mm x 120 mm x 10 mm.

Density of mild steel = 7,300 kg/m³

Volume = 100 x 120 x 10 = 120,000 mm³

Volume in m³ =  = 0.00012 m³

Remember: There are 10   mm³ in 1 m³

Mass = Volume x Density

= 0.00012 x 7,300

= 0.876 kg

# Self Assessment

Questions on Background Notes – Module 4.Unit 14

1.     What is the density of water?

2.    What volume does 1kg of water occupy?

3.    How do you get the true length of a line?

4.    Why use triangulation to develop a cone?

5.     Calculate the volume of water in a pipe of diameter 200mm and height of 60mm.

# Answers to Questions 1-5. Module 4.Unit 14

1.

Water is always shown with a specific gravity/relative density of 1.0.

2.

1 kg of water occupies a volume of 1 litre.

3.

Plan length against the vertical height.

4.

Sometimes the apex is a great distance from the base making the development awkward and wasteful of material.

5.

Volume (R² x H 3.142 x 100² x 60 = 31420 x 60 = 1,885,200mm³ = .0018852m² Volume in litres = .0018852 x 1,000 Answer = 1.8852 litres 1 litre = 1,000,000mm³

# Index

D

Density, 10

Density, 12

Relative Density (Specific Gravity), 12

To Find the Density of an Irregular Solid, 11

M

Mass, Volume, Density, 14

P

Physical Properties of Materials, 13

R

Right Cone (Radial Line), 9

S

Self Assessment, 16

T

Triangulation, 9