| Trade of Sheet Metalwork |
| --- |
| Module 4: | General Sheet Metalwork |
| Unit 11: | On-Centre Round to Square |
|  | Phase 2 |

Table of Contents

List of Figures	4

List of Tables	5

Document Release History	6

Module 4 – General Sheet Metalwork	7

Unit 11 – On-Centre Round to Square	7

Learning Outcome:	7

Key Learning Points:	7

Training Resources:	7

Key Learning Points Code:	7

On-Centre Round to Square	9

Area of Circle	10

Example 1	11

Conversion between Units of Area	13

Example 2	13

Volume	14

Example 1	14

Volume and Surface Area – Prisms	15

Example 2	15

Self Assessment	16

Answers to Questions 1-3. Module 4.Unit 11	17

Index	18

# List of Figures

Figure 1 - On-Centre Round to Square	8

Figure 2 - 1/2 Pattern	9

Figure 3 - Area of Circle	10

Figure 4 - Dimension, Perimeter and Area Calculation	11

Figure 5 - Volume 1	14

Figure 6 - Volume 2	14

Figure 7 - Triangular Prism	15

# List of Tables

# Document Release History

| Date | Version | Comments |
| --- | --- | --- |
| 20/11/06 | First draft |  |
| 09/01/07 | Implemented edits from Brendan Deasy. |  |
| 09/04/14 | 2.0 | SOLAS transfer |

# Module 4 – General Sheet Metalwork

## Unit 11 – On-Centre Round to Square

Duration – 10.5 Hours

### Learning Outcome:

By the end of this unit each apprentice will be able to:

Read and interpret drawings involving triangulation

Organise the production sequence

Mark out and fabricate a concentric square to round using the triangulation method

### Key Learning Points:

| D | Drawing and development of a central square to round. |
| --- | --- |
| Sk | Shaping and forming of transformers. |
| M | Mathematical problems involving multiplication and division. |

### Training Resources:

Toolkit

0.8mm mild steel

Tools and machinery/equipment

Notepad

Job card

Safety equipment and protective clothing

### Key Learning Points Code:

M = Maths	           D= Drawing     RK = Related Knowledge Sc = Science

P = Personal Skills	Sk = Skill	   H = Hazards

Figure 1 - On-Centre Round to Square

# On-Centre Round to Square

- The only difference between the previous job and this one is the round part is bigger. We use triangulation and the pattern should look like this.

- This square to round (or round to square) has a flat piece at one end to facilitate fitting a flange. It has to be notched at corners Band C.

- Place your square along edge A B and scribe a line from Z out to edge. Place square along edge B C and again scribe a line out to the edge. The same is done at R.

- When fabricating bend the lines A¹ - Z, Z - R and R - D¹ first. Bend them down very slightly.

- Next bend lines 6 - Z, 3 - Z, 3 - R and 0 - R very lightly in an upward direction. We then shape the part over a round bar.

Figure 2 - 1/2 Pattern

# Area of Circle

If we were to divide a circle into a very large number of very thin triangles as shown below and then rearrange them as shown underneath, we would obtain a figure which is very nearly a rectangle of length, half the circumference (πr) and height equal to the radius (r).

Figure 3 - Area of Circle

Area of Rectangle = π r x r = π r ²

## Example 1

Find the dimension Z, perimeter and area of the figure shown in the sketch below.

Figure 4 - Dimension, Perimeter and Area Calculation

Dimension Z:

Radius of each end r = 2.5  2 = 1.25m

Z = 7m - 2r = 7 - 2.5 = 4.5m

Perimeter:

= 2Z + πD

= 2 x 4.5 + 3.14 x 2.5 = 16.85m

Area:

Circle + Rectangle

= πr² + 2.5 x Z

= 3.14 x 1.25² + 2.5 x 4.5 = 16.15625

= 16.16m²

Test Yourself

Determine the area of the face of the V-Block shown in the sketch below.

Answer:

Dimension	Z = 100 - 20 = 80mm

X = 80 – 10 = 70mm

Area 		= Circle + Rectangle - 2 Circles

= π x 10² + 80 x 20 - 2 x π x 5²

= 314 x 1600 - 157

= 1757mm²

## Conversion between Units of Area

There are 1000mm in 1 metre.

One square metre contains:

1000 x 1000 = 1,000,000mm².

1,000,000 (1 million) is a very large number and is often written as 10 , the 6 represents the number of 	zeros after the initial 1.

## Example 2

1 in. = 25.4 mm. Estimate the number of square mm (mm²) in 1 square inch (1 in²):

1 in x 1 in = 1 sq. inch

25.4 x 25.4 = 645.16 mm²

1 in² = 645.14 mm²

Test Yourself

Determine the number of mm² in a circle of radius 2 in.

Answer:

2 in = 2 x 25.4	= 50.8 mm

Area of circle 	= π r²

= 3.14 x 50.8²

= 8103 mm²

# Volume

The volume of a solid, liquid or gas is a measure of the space it occupies.

The unit of volume is the cubic metre. It is the space occupied by a cube with edges 1 m as shown below.

Figure 5 - Volume 1

In finding the volume of a figure we need to know how many cubic units are contained in that figure. A rectangular solid is a familiar and simple figure to start with.

## Example 1

Calculate the volume in cubic metres of a room 3m high x 3m wide x 4m long as shown in Figure 6.

Figure 6 - Volume 2

From the sketch one may observe that the volume is 36m². In general, the volume of a rectangular solid is the product of its length, width and height.

## Volume and Surface Area – Prisms

A Prism is a solid object which has exactly the same cross-section throughout its length. Thus a triangular prism, shown in Figure 7, is a solid object with a triangular cross-section throughout its length.

Figure 7 - Triangular Prism

## Example 2

Determine the cross-sectional area and the volume of the prism shown above.

Cross-Sectional Area:

= Area of Triangle =

Volume:

= 6 x 7 = 42m³

# Self Assessment

Questions on Background Notes – Module 4.Unit 11

1.     How many mm² in a square metre?

2.    How many mm in an inch?

3.    Find the volume of the prism.

# Answers to Questions 1-3. Module 4.Unit 11

1.

One square metre contains: 1,000 x 1,000mm = 1,000,000mm²

2.

25.4mm are in an inch.

3.

Cross sectional area = = 12m² Volume = 12m² x 10 = 120m³

# Index

A

Area of Circle, 11

Conversion between Units of Area, 14

Example 1, 12

Example 2, 14

O

On-Centre Round to Square, 9

S

Self Assessment, 17

V

Volume, 15

Example 1, 15

Example 2, 16

Volume and Surface Area - Prisms, 16