# MODULE 1 - Induction and Bench Fitting

## Unit 6 – Filing Internal & External Radii

### Questions

- State the Pythagoras Theorem.

- What are the advantages of using absolute dimensioning over incremental 
 	dimensioning.

- Give an example of line and end measurement?

- What is a surface roughness comparator chart used for?

- What is the meaning of the Ra value.

### Answers

1. 	The theorem states that for a right angled triangle the square on the hypotenuse 
 	(longest side) is equal to the sum of the squares on the other two sides.

2. 	Absolute dimensioning is more accurate and can be marked out easily from the 
 	drawing, because all the features are measured from one edge. In incremental 
 	dimensioning the positions have to be calculated before marking out and 
 	measuring. Also as each hole, for example, has its own positional tolerance, then 
 	there can be a build up of tolerances and therefore is less accurate then absolute 
 	dimensioning.

3. 	An example of line measurement is the rule which can be used to measure a 
 	component. Examples of end measurement are the vernier calipers and 
 	micrometer.

4. 	A surface roughness comparator chart can be used to compare the surface of a 
 	workpiece to that of a standard sample. The comparator chart consists of a range 
 	or machined samples and the corresponding Ra value.

5. 	The Ra value is the average height of the peaks and valleys on a metal 
 	surface, at the micro scale (0.001mm).