# MODULE 6 – CNC Tools

## Unit 1 – CNC Machine Tools

### Questions

- What is the meaning of CNC?

- What is the difference between the Slideways on conventional machine  compared to those of a CNC machine?

- How is swarf removed on high production CNC machines?

- How are the tables and spindle driven on a CNC machine?

- Explain the difference between the open-loop system and the closed-loop system?

### Answers

- CNC means Computer Numerical Control.

- The slideways on a conventional machine operate under the conditions of 
 	sliding friction, where the friction is higher at lower velocities, which can 
 	result in jerky slide movements. To overcome this rolling friction can be used 
 	instead of sliding friction, where re-circulating roller bearings are positioned 
 	under the slideways.

- Some CNC machines have built in swarf removal equipment such as rotary 
 	screw or linear conveyors. Slanted beds in CNC lathes allow swarf to fall 
 	away into the base of the machine.

- The slides and spindle of the CNC machine are driven by either stepper 
 	motors or servo motors.

- With the open loop system a digital signal is sent from the controller to the   
 	Stepper Motor, which causes the slide to move by the required distance. There 
 	is no feed back, therefore there is no means of comparing the final position to 
 	the position in which it was commanded to go.

In the closed-loop system a digital signal is sent from the controller to the   
 	Servo Motor, which causes the slide to move by the required distance. The 
 	actual position and velocity of the slideway is continuously compared to the 
 	digital signal that is being sent out by the controller.